11 January 2010

Draft

STATUTORY INSTRUMENTS

S.I. No --- of 2010

______________________

Safety, Health and Welfare at Work

(Mines) Regulations 2010

S. I. No --- of 2010

SAFETY, HEALTH AND WELFARE AT WORK (MINES) REGULATIONS 2010

ARRANGEMENT OF REGULATIONS

PART 1

Preliminary and General

1. Citation and commencement.

2. Interpretation.

3. Meaning of mine.

4. Application.

5. Amendment of Safety, Health and Welfare at Work (Extractive Industries) Regulations 1997.

PART 2

Safety and Health Management

6. Appointment of operator.

7. Appointments before commencement of mining operations.

8. Notifications to Authority.

9. General duties of operator.

10. Management structure.

11. Qualifications of Mine Manager.

12. General duties of Mine Manager.

13. Safety statement.

14. Co-ordinated measures.

15. Safety induction, competence and skills certification.

16. Qualifications of deputy (shiftboss).

17. Deputy’s certificate.

18. Duties of deputy.

19. Instructions, rules and operating procedures.

20. Permits to work.

21. Duties of persons at work.

22. Mine safety representative.

23. Consultation.

24. Record keeping.

PART 3

Inspection and Supervision

25. Inspection, maintenance and testing schemes.

26. Supervision of work.

27. Pre-shift inspections.

28. Inspections during shifts.

PART 4

Roads and Vehicles

29. Construction and equipment of vehicles.

30. Inspection and maintenance of vehicles.

31. Appointment of drivers.

32. Carrying of passengers.

33. Road surfaces.

34. Roadway clearances.

35. Gradients.

36. Safety of pedestrians in roadways.

37. Vehicle and traffic rules.

38. Safeguarding edges of excavations and lagoons.

39. Danger areas.

40. Traffic routes.

41. Outdoor workstations.

42. Protection from falling objects and provision of safety helmets.

43. Prevention of drowning.

PART 5

Ventilation

44. Duty to provide adequate ventilation.

45. Main ventilation fan.

46. Additional underground fans .

47. Auxiliary ventilation.

48. Prevention of leakage.

49. Ventilation rules.

PART 6

Stability and Ground Support

50. General duty to ensure safety of excavations, tips, and lagoons.

51. Operating procedures for excavations, tips and lagoons.

52. Stability of roads and working places.

53. Duty of persons at work in a mine.

54. Scaling of roof and sides.

55. Working at or near unsupported stopes.

56. The use of backfill material as a means of support.

57. Ground support rules.

58. Appraisal and site investigation of excavations, tips and lagoons.

59. Geotechnical assessments.

PART 7

Explosives

60. Application of Part 7.

61. Appointment of explosives supervisors, shotfirers and storekeepers.

62. Scheme of transit for explosives.

63. Storage, transport, use and disposal of explosives or ANBI.

64. Shotfiring rules.

65. Blast specification.

66. Shotfiring operations.

67. Duties of explosives supervisor and shotfirer.

68. Misfires.

69. Prohibited activities.

70. Records of explosives.

PART 8

Electricity

71. General.

72. Protection of cables.

73. Introduction of electrical equipment.

74. Restriction of certain categories of electrical equipment in certain zones below ground.

75. Cutting off electricity or making safe where flammable gases are found.

76. Means of cutting off electricity to circuits below ground.

77. Schematic diagrams.

78. Electric shock notices.

79. Storage, charging and transfer of electrical storage batteries.

80. Leakage protection.

81. Reportable incidents.

82. New installations and major alterations.

PART 9

Access, Egress and Emergency Planning

83. Outlets and workings.

84. Ladderways between working levels.

85. Entrances to shafts, staple pits, ore passes and stopes.

86. Pedestrian and Vehicle traffic routes.

87. Escape and rescue facilities.

88. Safety drills.

89. Fire and explosion hazards.

90. Explosive or harmful atmospheres.

91. Lighting.

92. Prevention of unauthorised entry.

93. Means of evacuation.

94. Underground workforce accounting.

95. Precautions for withdrawal of employees.

96. Precautions against external dangers to workings.

97. Precautions in case of outbreak of fire.

98. Inspection of fire-fighting equipment.

99. Warning of emergencies.

100. Refuge stations.

101. Rescue teams.

102. Composition of rescue teams.

103. Training of rescue workers.

104. Equipment to be provided for rescue work.

105. Fresh air base.

106. Rescue plans.

107. Incident controller.

108. Emergency procedures.

PART 10

Preparation of Mine Plans

109. Appointment and qualifications of mine surveyor.

110. Duties of mine surveyor.

111. Scale, datum and other details required on plans.

112. Additional plans.

113. Keeping of plans.

114. Faulty plans.

Part 11

Provisions Relating to Hoisting Systems (Including Shafts)

115. Appointment and hours of work of hoistman.

116. Hoisting Rules.

117. Hoist controls, instrumentation and position indicators.

118. Breaking systems.

PART 12

Special Provisions Relating to Gaseous Mines

119. Protection from explosion risks.

120. Gassy mines.

121. Mines containing flammable dusts.

122. Electrical equipment at gassy mines or mines containing flammable dusts.

123. Fires, spontaneous combustion and heatings.

124. Gas outbursts, rock bursts and water inrushes.

125. Protection from harmful atmospheres.

126. Safety equipment.

PART 13

Air Receivers

127. Definition of “air receiver”.

128. Safety precautions.

129. Maintenance and examination.

PART 14

Safety Provisions for Ancillary Activities and Installations

130. Definition of “place of work” (Part 14).

131. Stability and solidity.

132. Floors, walls and ceilings of rooms.

133. Room dimensions, air space in rooms and freedom of movement at workstations.

134. Windows and skylights.

135. Doors and gates.

136. Ventilation in rooms.

137. Temperature in rooms.

PART 15

Health

138. Health surveillance.

139. Medical examinations.

140. Health hazards.

141. Atmospheric influences.

142. Disposal of waste.

143. Stationary internal combustion engines and exhaust gases.

PART 16

Welfare

144. Shelters and accommodation for clothing and taking meals.

145. Changing rooms and lockers.

146. Washing facilities.

147. Sanitary conveniences.

148. Safe access to places where facilities are provided.

149. Pregnant women and nursing mothers.

150. Persons with disabilities.

151. Rest rooms.

SCHEDULES

Schedule 1: Notifications to the Authority

Schedule 2: Mines Skills Training Scheme

Schedule 3:- Inspection Report Forms

Schedule 4: Procedures for the Selection of a Mine Safety Representative

Schedule 5: Vehicles Requiring Auxiliary Devices and Visual Aids

Schedule 6: Geotechnical Assessments

Schedule 7: Hoisting Rules

Schedule 8: Air Receivers

Schedule 9: Certificate of Medical Examinations

Safety, Health and Welfare at Work (Mines) Regulations 2010

I, ……….., Minister of State at the Department of Enterprise, Trade and Employment, in exercise of the powers conferred on me by section 58 of the Safety, Health and Welfare at Work Act 2005 (No. 10 of 2005) and the Enterprise, Trade and Employment (Delegation of Ministerial Functions) (No. 2) Order 2009 (S.I. No. 249 of 2009), and for the purpose of giving effect to Council Directive 92/104/EEC of 3 December 1992, after consultation with the Health and Safety Authority, hereby make the following regulations:

PART 1

Preliminary and General

Citation and commencement.

1. 	(1) These Regulations may be cited as the Safety, Health and Welfare at Work (Mines) Regulations 2010.

(2) These Regulations shall come into operation on ……….. 2010.

Interpretation

2. 	(1) In these Regulations-

"Act" means the Safety, Health and Welfare at Work Act, 2005, (No.10 of 2005);

"Act of 1875" means the Explosive Act 1875 (38 & 39 Vict., c. 17);

“ammonium nitrate blasting intermediate, (ANBI)” means non-sensitised mixtures of, primarily, ammonium nitrate and other substances which are not themselves explosive, such as oxidisers and fuels, intended to produce a blasting explosive (or agent), only after further processing prior to use, and classified in accordance with the United Nations Recommendations as falling within Class 5.1.

“ancillary surface installation" means any surface installation housing workstations which are essential to the operation of an underground mine and include, crushing, screening and sizing processes, surface explosive and detonator stores, surface ventilation fan installations and airlocks, tailings management facilities, stockpiles and tips, but shall not include milling of ore, chemical or thermal processing of ore, surface workshops or offices;

"appoint" in relation to a person, means appoint in writing with a written statement summarising his or her responsibilities and duties and "appointed" shall be construed accordingly;

"auxiliary fan" means a fan used or intended to be used below ground in a mine wholly or mainly for ventilating a heading, drift or blind end;

"blasting agent" means a mixture intended for blasting consisting substantially of inorganic nitrates and carbonaceous combustibles in which none of the ingredients is a commercial explosive and which cannot be detonated by a No. 8 Detonator;

“breathing apparatus" means apparatus of such a character that it supplies all the requirements of respiration by itself and is independent of the surrounding atmosphere;

"charge" means explosive which may be exploded by a single detonator or primer, or a blasting agent which may be exploded by a primer;

"circuit" means part of an electrical installation supplied from the same origin, which may be protected against overcurrents by the same protective device;

"circuit breaker" means an electro-mechanical device capable of making, carrying and breaking currents under normal circuit conditions and also capable of making, carrying for a specified time, and breaking currents under specified abnormal circuit conditions such as those of short circuit;

"conductor" means a conductor of electrical energy;

"danger" in relation to Part 8 means risk of death or personal injury or risk to health from electric shock, electric burn, electrical explosion or arcing, or from fire or explosion caused by the use of electricity or from mechanical movement of electrically driven equipment;

"deputy (shiftboss)" means a person appointed as a deputy (shift boss) pursuant to Regulation 16 who holds the requisite qualifications or is in possession of a certificate issued pursuant to Regulation 31 of the Mines (Managers and Officials) Regulations 1970(S.I. No. 74 of 1970);

"detonator" means an initiator for explosives that contains a charge of high explosive fired by means of a flame, spark, electric current or shock tube;

"detonator case" means a waterproof bag or other suitable container for carrying detonators;

"detonator store" means an explosive store used exclusively for the storage of detonators in bulk.

"earthing" means the connection of the exposed conductive parts of an electrical installation to the conductive mass of the earth and earthed shall be construed accordingly;

“excavation” means any place at a mine where minerals are being or have been extracted and includes the floor, faces or sides of that place;

"electrical equipment" includes any conductor or electric cable and any part of any machine, apparatus or appliance, intended (in any case) to be used or installed for use for the generation, transformation, conversion, switching, controlling, regulating, rectification, storage, transmission, distribution, provision, measurement or use of electrical energy;

"electrical installation" means an assembly of associated electrical equipment fulfilling a specific purpose or purposes and having coordinated characteristics;

"exploder" means a device designed for firing detonators;

"explosives" means Class 1 explosives as classified in the manual published by the United Nations Organisation and entitled “Fifteenth Revised Edition of the Recommendations prepared by the United Nations Committee of Experts on the Transport of Dangerous Goods” (ISBN 92-1-139120-6) or a later edition thereof that is in substitution for, and not an alternative to, that edition;

"explosive article" means an article containing one or more explosive substances;

"explosives store" means any of the following:

(a) a magazine licensed under sections 6 to 8 of the Act of 1875, and

(b) a store licensed under section 15 of that Act,

“explosive substance” means a solid or liquid substance (or a mixture of those substances) that is, by itself, capable by chemical reaction of producing gas at such temperature, pressure and speed as could cause damage to its surroundings;

“explosives supervisor” means a person appointed under Regulation 61 to organise and supervise all work involving explosives;

"fresh air base" is a place within the mine that is determined by a competent person at that time to be in a breathable atmosphere and is suitable for use as a base for rescue work during rescue operations where there is, or may be, an irrespirable atmosphere;

"flexible cable" means an electric cable which is designed to be moveable while in use;

"gas" includes fume or vapour;

"geotechnical assessment" has the meaning given to it in Regulation 59;

“geotechnical specialist” means a professional engineer or professional geologist competent to carry out a geotechnical assessment under Part 6;

"high voltage" means any voltage exceeding 1,000 volts alternating current or 1,500 volts direct current;

"incendive sparking" means in relation to any electrical equipment sparking in such circumstances that inflammable gas present in the air outside the equipment might be ignited directly or indirectly;

"insulating material" means non-conducting material enclosing, surrounding or supporting a conductor or any part thereof, and which is of such quality and thickness as to prevent danger;

"insulation resistance" means the resistance between two conductors or systems of conductors normally separated by insulation o, the resistance between any such conductor and earth;

"isolation" means the disconnection and separation of electrical equipment from every source of electricity in such a way that the disconnection is secure, and isolated shall be construed accordingly;

"lagoon" means any natural or artificial pond or tailings pond (including any water-filled excavation) used in connection with mining operations and includes-

(a) such a pond that treats waste water utilising sunlight, bacterial action and oxygen to purify that water, and

(b) a place at a mine where waste water, sludge and liquid waste accumulate or are stored;

"live" in relation to Part 8 means electrically energised;

"locomotive" means a mechanically propelled vehicle running on rails, constructed or used for hauling other vehicles and being a locomotive to which these regulations apply;

"main intake airway" means either a length of intake airway which begins at a shaft or at an outlet and ends at a working face or a length of airway in which at the inner end, the current of air in the airway is split and which as regards two or more working faces is an intake airway;

"main return airway" means either a length of return airway which begins at a working face and ends at a shaft or at an outlet, or a length of airway in which at the inner end, there is a junction of two or more currents of air and which as regards two or more working faces is a return airway;

"mechanically propelled vehicle" means a wheeled or tracked mechanically driven mobile plant (including mobile plant used for the loading, transporting, or haulage of minerals, materials or for the carriage of persons) which forms part of the equipment of the mine other than a locomotive;

“mine” has the meaning given to it by Regulation 3;

“mine manager” means an individual appointed under Regulation 10 to manage the operation of a mine;

“mine owner” means the owner of a mine, or part of a mine;

“minerals” means any natural deposit, including stone, slate, clay, gravel and sand, and includes products of minerals, but does not include petroleum within the meaning of Part II of the Petroleum and Other Minerals Development Act 1960 (No. 7 of 1960) or peat;

"misfire" means an occurrence in relation to the firing of shots where -

(a) testing before firing reveals broken continuity which cannot be rectified, or

(b) a shot or any part of a shot fails to explode when an attempt is made to fire it;

“operator”, in relation to a mine, means an employer or other person who has been appointed under Regulation 6 by a mine owner;

"overcurrent" means any current exceeding the rated value;

"overhead line" means any electric line or telephone line which is placed above ground and suspended in the open air;

"permitted detonator" means, in relation to a mine or any part of a mine, a category of detonator suitable for use where there is deemed to be a risk of an explosive atmosphere;

"permitted explosives" means, in relation to a mine or any part of a mine, a category of explosives suitable for use where there is deemed to be a risk of an explosive atmosphere;

"permitted lights" means, in relation to a mine or any part of a mine, a category of light suitable for use where there is deemed to be a risk of an explosive atmosphere;

"place of transfer" means a safe and secure place on the surface, designated by the mine manager for the transfer of explosives from delivery vehicles to designated explosives vehicles, for immediate conveyance to an underground explosives store, underground detonator store, reserve station, or to a working place for immediate use.

"portable equipment" means equipment (including handheld portable equipment) which, because of the manner in which it is to be used, requires to be moved while it is working, or is designed so that it can be moved while it is working or is moved from time to time between the periods during which it is working;

“Principal Regulations” means the Safety, Health and Welfare at Work (General Application) Regulations 2007 (S.I. No. 299 of 2007) as amended by the Safety, Health and Welfare at Work (General Application)(Amendment) Regulations 2007 (S.I. No. 732 of 2007);

"prospecting" means the activity of searching for minerals or mineral deposits;

"refuge station" is a place below ground separated from adjoining workings by closeable openings containing sufficient quantities of air and water and so equipped so that products of combustion can be prevented from entering it and enabling it to sustain the lives of persons taking refuge within it;

"reserve station" means a suitable place below ground for the issue and return and temporary storage of either explosives, or detonators or ANBI, which is situated at a safe distance apart from any other reserve station or explosives store;

"residual current device" means an electro-mechanical switching device intended to disconnect a circuit when the residual current attains a stated value under specific conditions;

"retraining" means the reacquisition of necessary skills by a person who had undergone previous training in such operation or operations;

"road" means a road below ground in a mine in which persons travel or in which vehicles, including locomotives, operate and includes part of a road but does not include an unwalkable outlet;

"safety fuse" means a cord that contains an internal burning medium by which fire is conveyed at a continuous and uniform rate for the purpose of firing detonators or blackpowder, without initiating burning in a similar fuse that may be in lateral contact alongside;

"scheme of transit" shall be construed in accordance with Regulation 62;

"self-rescuer" means a device carried on the person of each miner or within the vehicle the miner is operating that can provide the miner with a supply of oxygen to enable him or her to travel and escape from a potentially unbreathable atmosphere to either a fresh air base, a refuge station or to the surface of the mine;

"shaft" means a shaft at the top of which is, or is intended to be, at the surface;

"shiftboss" means a person appointed as a shift boss (deputy) pursuant to Regulation 16 who holds the requisite qualifications or is in possession of a certificate issued pursuant to Regulation 31 of the Mines (Managers and Officials) Regulations 1970;

"shot" means a single shot or a series of shots fired as part of one blast;

"shotfirer" means a person appointed under Regulation 61 to be responsible for shotfiring operations;

“shotfiring operations” includes any of the following:

(a) checking to ensure that the blast specification is still appropriate for the site conditions at the time the blasting is to take place,

(b) checking the geometry of shotholes,

(c) mixing explosives, including the manufacture of blasting agents by blending ANBI and a sensitiser,

(d) priming a cartridge,

(e) charging and stemming a shothole, includes pumping mixed AnFo, ANBI and a sensitiser, into shotholes using underground pumping units.

(f) linking or connecting a series of shots,

(g) withdrawal and sheltering of persons,

(h) inspecting and testing a shotfiring circuit,

(i) firing a shot,

(j) checking for misfires,

(k) destroying surplus explosives;

“shotfiring rules” means rules made under Regulation 64;

"staple pit" includes winze;

"stope" means any excavation made in a mine  to remove ore that has been rendered accessible by the development of shafts and drifts;

"storage battery vehicle" is a mechanically propelled vehicle in which the motive power is generated by an electric motor supplied from a storage battery;

"storage battery locomotive" means a locomotive in which the motive power is generated by an electric motor supplied from a storage battery;

“storekeeper” means a person appointed under Regulation 61 to be responsible for the safe operation of an explosives store;

"substation" means any building, enclosure or other structure (or part thereof) which is large enough to enable a person to enter after the electrical equipment therein is in position and which contains equipment for transforming or converting electrical energy either to or from high voltage (not being equipment for transforming or converting electrical energy solely for the operation of switchgear or instruments) and includes the said equipment for switching, controlling or otherwise regulating electrical energy;

“tip” means an accumulation or deposit of minerals used in connection with mining operations and includes –

(a) overburden dumps, backfills, spoil heaps, stock piles and any wall or structure that retains or confines a tip, and

(b) a tip that had been used during previous mining operations and from which minerals are being extracted for further use or for sale;

“trainee shotfirer” means a person appointed under Regulation 61 for the purpose of undergoing training in shotfiring operations under the close personal supervision of a shotfirer;

"transportable equipment" means equipment which, from the nature of its use, requires to be moved to a new position from time to time between the periods when it is working;

"traveling road" means a length of road in a mine, used for the purpose of walking or driving to or from working places;

"unwalkable outlet" means an outlet which, owing to the gradient thereof or of any part thereof, (whether alone or in combination with other circumstances), persons cannot walk up with reasonable convenience;

“vehicle and traffic rules” means rules made under Regulation 37;

"winding apparatus" means, in relation to a mine shaft or staple pit, apparatus for lowering and raising loads through the shaft or staple pit;

"working area" means all of the working places in a mine which are below ground and in which workers in the charge of a deputy (shiftboss) are deployed by him or her for the performance of their duties (including an area of responsibility or district, where districts are delineated at the mine,) and includes any immediate means of access and egress thereto;

“workstation” means any location at a mine where work or work-related activities are undertaken.

(2)	Where, under these Regulations, a person is required to make instructions, rules, operating procedures or schemes, such instructions, rules, operating procedures or schemes, as the case may be, shall be set out in writing and reasonable in the context of the duty that the person is required to carry out.

Meaning of “mine”.

3.	(1)	In these Regulations “mine” means, subject to paragraph (2), an excavation or system of excavations made for the purpose of, or in connection with, the extraction, wholly or substantially by means involving the employment of persons or machinery (or both) below ground, of minerals or prospecting with a view to such extraction and includes any of the following:

(a)	so much of the area (including works thereon and ancillary surface installations such as buildings and other premises and structures providing accommodation, rest and sanitary facilities) adjacent to or surrounding mining operations as is occupied for the purpose of, or used in connection with -

(i)	those operations,

(ii)	the storage or preparation for sale of the minerals extracted from the mine, or

(iii)	the removal from the mine of any substance extracted from the mine;

(b)	a tip;

(c)	a lagoon or tailings pond;

(d)	a railway line or siding at the mine.

(2)	Notwithstanding paragraph (1), “mine” does not include any of the following:

(a)	an excavation or system of excavations made in the carrying out of construction work within the meaning of the Safety, Health and Welfare at Work (Construction) Regulations (S.I. No. 504 of 2006);

(b)	a public road;

(c)	an area of a mine at which any manufacturing process (including the processing of minerals) other than the manufacturing of ammonium nitrate mixtures under license from the Minister for Justice, Equality and Law Reform is carried out;

(d)	an area of a mine that is being used exclusively for a work activity unconnected with the extraction of minerals, or the preparation for sale of minerals.

Application.

4.	(1)	Subject to paragraph (2), these Regulations apply to all mines.

(2)	These Regulations do not apply to a mine in relation to which -

(a)	notice of permanent cessation of mining operations has been given to the Authority in accordance with Regulation 8, and

(b)	all work relating and incidental to that cessation has been completed, including work for the purpose of preventing unauthorised entry into the mine and the escape from that mine of water or other substance that flows when wet.

(3)	The relevant statutory provisions apply to all mines, without prejudice to more stringent or specific provisions contained in these Regulations.

Amendment of Safety, Health and Welfare at Work (Extractive Industries) Regulations 1997.

5.        	The Safety, Health and Welfare at Work (Extractive Industries) Regulations 1997 (S.I. No. 467 of 1997) are further amended by inserting after Regulation 3A the following Regulation:

“Non-application to mines

3B.	Notwithstanding Regulations 2(1), 3 and 3A, these Regulations shall not apply to a mine within the meaning of the Safety, Health and Welfare at Work (Mines) Regulations 2010.”.

PART 2

Safety and Health Management

Appointment of operator.

6. 	(1) Before the commencement of operations at a mine, or part of a mine -

(a)	the mine owner shall appoint a competent person who has sufficient resources to be the operator of the mine, or part of the mine, as the case may be, or

(b)	where the mine owner is competent and has sufficient resources to do so, he or she may appoint himself or herself as operator of the mine, or part of the mine

and shall make a record of the appointment.

(2)	Where the mine owner under paragraph (1) (a) appoints another person to be the operator of the mine, or part of the mine, both parties shall sign the record and the mine owner shall provide a copy of the signed record to the operator.

(3)	The original record and a signed copy of it shall be kept by the mine owner and the operator, respectively, for a period of 6 years from the termination of the operator’s appointment as operator of the mine, or part of the mine.

(4)	The mine owner shall provide the operator with any relevant information available to him or her, which might affect the safety, health and welfare of persons at work at the mine.

(5)	Where the mine owner appoints different operators for different parts of a mine, the owner shall -

(a)	appoint one of them to be the common operator for the purposes of Regulation 14, and

(b)	demarcate the different parts of the mine.

Appointments before commencement of mining operations.

7.	No person shall be deployed to carry out mining operations at a mine unless-

(a) an operator has been appointed under Regulation 6,

(b) a mine manager has been appointed under Regulation 10, and

(c) a sufficient number of mine deputies have been appointed under Regulation 10.

Notifications to Authority.

8.	(1)	The operator shall ensure that written notice as specified in Form M1 set out in Schedule 1 is given to the Authority not later than 14 days following the occurrence of any of the following events in respect of the mine:

(a) his or her appointment as operator;

(b) his or her appointment as the common operator;

(c) the appointment of mine a manager;

(d) the commencement of mining operations;

(e) the permanent cessation of mining operations.

(2) 	The operator shall ensure that written notice of dangerous occurrence as specified in Form M2 set out in Schedule 1 is given to the Authority as soon as practicable following the occurrence of any of the following classes of occurrences at a mine which is not reportable by reason of death or injury in relation to that occurrence, that is to say, occurrences in which -

(a) any gas, other than gas in a safety lamp or other controlled use, or dust is ignited below ground,

(b) a fire breaks out below ground,

(c) a person, in consequence of smoke or any other indication that a fire may have broken out below ground, has been caused to leave any working area,

(d) a fire breaks out on the surface endangering the operation of—

(i) any winding or haulage apparatus installed either at or in a shaft of the mine or at or in an unwalkable outlet from the mine, or

(ii) any mechanically operated apparatus for producing ventilation below ground in the mine,

(e) there is any violent outburst of gas, mineral, ore, or other solid matter into the mine workings not being such an outburst which is caused intentionally,

(f) there is an inrush of noxious or flammable gas from old workings,

(g) there is an inrush of water, unintended release of backfill or the inrush of any material which flows when wet,

(h) a rope, chain, coupling or other gear of similar kind, by means of which persons are carried through a shaft, staple-pit or unwalkable outlet, breaks,

(i) a rope, chain, coupling or other gear of similar kind, used for the transport of persons below ground, breaks,

(j) any cage used for the carriage of persons is overwound while being so used,

(k) any cage not being used for the carriage of persons is overwound and becomes detached from its winding rope,

(l) any cage operated by means of the friction of a rope on a winding sheave is brought to rest by the apparatus provided for bringing the cage to rest in the event of its being overwound (such apparatus being sited either in the headframe of the relevant shaft or in the part of such shaft which is below the lowest landing for the time being in use),

(m) there is an explosion from, or collapse or burst of, any apparatus which is used either for generating a pressure of air, gas or steam greater than atmospheric, or for storing air, gas or steam at such a pressure,

(n) any ventilating apparatus (other than an auxiliary fan) breaks down thereby causing a substantial reduction in the ventilation of the mine lasting for a period exceeding thirty minutes,

(o) any headframe, winding engine house, screen house, tippler house or vehicle gantry collapses,

(p) any mechanically powered crane, crab or other lifting machine overturns, or any part thereof fails and causes the load of the machine to fall or, in case the machine has a jib, causes the jib to fall,

(q) breathing apparatus, a smoke helmet, self-rescuer or other apparatus serving the same purpose, while being used, fails to function safely or develops a defect likely to affect its safe working,

(r) immediately after using and arising out of the use of apparatus mentioned in subparagraph (q) a person receives first aid or medical treatment at the mine for resulting unfitness or suspected resulting unfitness,

(s) any unintentional ignition or explosion of explosives,

(t) a person, as a result of an explosion or discharge of any blasting material or device, suffers bodily injury and receives first aid or medical treatment at the mine,

(u) there is any movement of material, a fire or any other event indicating either that an accumulation or deposit of refuse, or that a settling pond forming part of the mine, is unstable or is likely shortly to become unstable,

(v) the uncontrolled movement, collision, overturning or runaway of any vehicle,

(w) the unintended movement of ground or fall of ground greater than one ton, or

(x) the unintended collapse or partial collapse of any structure.

General duties of operator.

9.	(1)	The operator shall, so far as is reasonably practicable, ensure that -

(a)	the mine and any machinery, tool or other article used at work there are, as appropriate, selected, designed, constructed, installed, equipped, commissioned, protected, operated and maintained in such a way that persons at work can perform the work assigned to them without endangering the safety, health and welfare of themselves or others,

(b)	if any of the articles referred to in subparagraph (a) is located in an area of the mine within which risk of fire or explosion from ignition of gas, vapour or volatile liquid exists, or is likely to exist, that article is -

(i)	suitable for use in that particular area, and

(ii)	if necessary, fitted with suitable protective devices and fail-safe systems,

(c)	mechanical equipment and plant at the mine is of adequate strength and free from patent defect and suitable for the purpose for which it is intended, and

(d)	electrical equipment and plant at the mine is of sufficient capacity for the purpose for which it is intended.

(2)	The operator shall ensure, as regards that mine, that -

(a)	work is planned and carried out taking into account the elements of the safety statement that concern the risks of falls, movements or slips of ground and, in particular, that -

(i)	the design and layout of mine workings, extraction faces, excavations and other areas is appropriate to the nature and stability of the ground and the methods of working,

(ii)	mine workings, pillars, hanging walls and haul roads are stable enough for the plant used and are constructed and maintained in such a way that plant can be moved safely,

(iii)	before the start or restart of work, the roofs, floors and sides of work areas and haul roads are checked for loose ground or rocks and scaling is carried out where necessary, and

(iv)	excavations and tips are not worked in such a way that instability is created,

(b)	it is organised so as -

(i)	to provide adequate protection against hazards,

(ii)	to be kept in good order, with any hazardous substances or deposits removed, and

(iii)	not to endanger the safety and health of persons at work,

(c)	workstations are designed and constructed according to ergonomic principles taking into account the need for persons at work to carry out their work safely and without risk to health at their workstations,

(d)	a sufficient number of persons with the requisite competence to perform the tasks assigned to them are present,

(e)	where a workstation is occupied by a person on his or her own, the necessary supervision or means of communication is provided, and

(f)	in the event of the permanent cessation of mining operations there, the mine is left, so far as is reasonably practicable, in a safe condition.

Management structure.

10.	(1) The operator shall establish a management structure that includes the appointment of -

(a)	subject to Regulation 11, a competent individual  as mine manager to -

(i)	manage the operation of the mine at all times when persons are working in the mine, provided that where the operator is an individual and is competent he or she may appoint himself or herself,

(ii)	advise the operator as to the observance of the requirements of the relevant statutory provisions, and

(iii)	exercise a general supervision of the observance of those requirements and the promotion of the safe conduct of work generally,

(b)	persons appointed under Regulation 61, and

(c)	an adequate number of deputies (shiftbosses), supervisors, officials, 	engineers, technicians and other competent persons -

(i)	to enable the mine to be inspected, operated and managed safely and in accordance with the safety statement,

(ii)	to supervise persons under their control at work at the mine,

(iii)  	to supervise persons engaged in work activities involving serious risk to safety and health as identified in the safety statement, and

(iv)	to visit workstations occupied by persons under their control at the mine at least twice during each shift, where this is specified as necessary under the safety statement.

(2)	The operator shall ensure that the management structure is reviewed regularly and revised where necessary and, in particular, if the mine undergoes significant changes (including natural changes), extensions or conversions.

(3)	The operator shall ensure that each person who forms part of the management structure is provided with a copy of those parts of the safety statement that describe that person’s authority and duties.

Qualifications of Mine Manager.

11.	The operator shall not appoint a person to be mine manager unless that person -

(a)	is at least twenty-six years of age,

(b)	has not less than three years appropriate underground practical experience in one or more mines

(c)	is the holder of, either

(i)	a recognised degree in mining engineering, or

(ii)	any other qualification of equivalent standard acceptable to the Authority.

General duties of Mine Manager.

12.	The appointed mine manager shall ensure, so far as is reasonably practicable, that -

(a) he or she has the management and control of all work activities at the mine, either directly or by his or her appointed deputies, supervisors and other officials, exercisable subject to any instructions given to him or her by the operator,

(b) a sufficient number of deputies, supervisors, officials, engineers and technicians are appointed at the mine to adequately inspect the mine and its equipment and to supervise all work at the mine,

(c) he or she and all appointed persons at the mine discharge their duties in respect of their appointment by the operator,

(d) all persons at the mine comply with all instructions, rules and operating procedures at the mine prepared by the operator,

(e) he or she advises the operator on the observance of the requirements of relevant statutory provisions,

(f) a suitable efficient system is established, operated and maintained to check-in persons going underground, to monitor the location of persons underground and to check out persons who have returned to the surface,

(g) a sufficient supply of suitable materials and equipment is at all times readily available for ensuring compliance with the relevant statutory provisions, and

(h) a competent substitute manager is appointed for any periods of his or her absence in excess of 48 hours from the mine.

Safety statement.

13.	(1)	The operator shall ensure that the safety statement, prepared in compliance with section 20 of the Act, includes details of the -

(a) management structure and appointments referred to in Regulation 10 setting out the duties and responsibilities of each person in the management structure,

(b) mines skills training scheme required by Regulation 15,

(c) operating procedures and instructions required by Regulation 19(a), relating to the safety and health of persons at work at the mine in both normal and critical situations there,

(d) arrangements for the review of safety measures in accordance with section 20 of the Act,

(e) system of permits to work, if required by Regulation 20,

(f) inspection, maintenance and testing schemes prepared in accordance with Regulation 25,

(g) vehicles and traffic rules required by Regulation 37,

(h) operating procedures for excavations, tips and lagoons required by Regulation 51,

(i) ground support rules required by Regulation 57,

(j) conclusions of any appraisal, site investigation or geotechnical assessment of an excavation, tip or lagoon undertaken pursuant to Regulations 58 and 59,

(k) shotfiring rules made under Regulation 64,

(l) instructions required by Regulation 87(c),

(m) precautions taken to protect against, detect and combat the outbreak and spread of fire required by Regulation 89,

(n) arrangements made and the equipment and measures necessary to prevent explosions required by Regulation 89,

(o) appointment of surveyor for the mine under Regulation 109,

(p) appointment of hoistman for the mine under Regulation 115,

(q) hoisting rules required by Regulation 116,

(r) arrangements for health surveillance required by Regulation 138.

(2)	In addition to the matters referred to in paragraph (1), the safety statement shall, where appropriate, also include -

(a) a plan detailing the equipment and measures required to protect persons at work at the mine from the risk of explosion or fire in compliance with Regulations 89 and 90(1),

(b) where toxic gases are or may be present in the atmosphere at the mine in such concentration that the atmosphere may be harmful to the health of persons at work, a plan detailing the protective equipment and measures required to protect persons at work at the mine from the harmful atmosphere in compliance with Regulation 90(2), and

(c) diagram of the mine indicating those areas to which these Regulations do not apply by virtue of Regulation 3(2).

(3)	The operator shall ensure that -

(a)	the measures identified in the safety statement are taken,

(b)	any plans included in that document are followed, and

(c)	each person in the management structure shall carry out the duties assigned to 		them in the safety statement so as to protect the safety, health and welfare of 		persons at work at the mine.

Co-ordinated measures.

14.	Without prejudice to section 21 of the Act, where a common operator has been appointed under Regulation 6(5), that operator shall co-ordinate the implementation of all measures relating to the safety, health and welfare of persons at work at the mine.

Safety induction, competence and skills certification.

15. 	The operator shall ensure that no person shall undertake any mining operations unless -

(a)	that person has received appropriate site-specific safety induction instruction,

(b)	that person is either competent to do that work, or does it under the instruction and supervision of some other person who is competent to give instruction in, and supervise the doing of, that work for the purpose of training that person,

(c)	if engaged in any of the tasks specified in the Mines Skills Training Scheme in Schedule 2,

(i)	that person holds an existing certificate of authorisation at the mine issued by the mine manager, or

(ii)	has been given the necessary 	training or re-training in accordance with the mines skills training scheme in Schedule 2 and has been issued, by the mine manager, with a certificate of authorisation for that task in respect of that mine as specified in Form M3 set out in Schedule 2.

(d)	a record of the training and re-training given and the issuing of each certificate of authorisation to each person employed at the mine is made and kept in accordance with Regulation 24.

# Qualifications of deputy (shiftboss).

16.  	The operator shall only appoint a person to be a mine deputy (shiftboss) and issue him or her with a deputy’s certificate if that person -

(a)	is at least twenty-one years of age,

(b)	has not less than three years appropriate practical underground experience in one or more mines,

(c)	holds a recognised qualification in occupational first aid,

(d)	has received training in shotfiring operations,

(e)       is the holder of either -

(i)	a diploma or degree in mining engineering, or

(ii)	any other qualification of equivalent standard acceptable to the Authority, or

(iii) 	has successfully completed a theoretical examination prescribed by the Authority.

Deputy’s certificate.

17.	An inspector may grant a certificate (in these Regulations referred to as a deputy’s certificate) to a person who the operator confirms in writing complies with the provisions of Regulation 16.

Duties of deputy.

18.	An appointed mine deputy (shiftboss) shall ensure, so far as is reasonably practicable, that -

(a) he or she has the management and control of all workers and all work activities within his or her working area, exercisable subject to any instructions given to him or her by the operator,

(b) all duties in respect of his or her appointment by the operator are discharged,

(c) all persons at work at the mine under his or her immediate charge and direct supervision comply with all instructions, rules and operating procedures at the mine prepared by the operator,

(d) within 2 hours immediately before the commencement of work in any part of their working area, carry out or have carried out by a competent person a pre-shift inspection to ascertain –

(i) the adequacy of ventilation,

(ii) the presence of toxic gases,

(iii) the stability of roofs, floors and sides, and

(iv) general safety,

save that where continuous working is being carried on the last inspection  by the deputy of the previous shift shall be sufficient for such pre-shift inspection if made at intervals not exceeding twelve hours,

(e) immediately following any pre-shift inspection a written record of that inspection is made as specified in Form M4, set out in Schedule 3, provided for the purpose by the operator,

(f) all working areas where persons under his or her immediate charge and direct supervision are carrying out work are visited at periods not exceeding four hours,

(g) during a shift at every working place, within his or her working area, which is required to be ventilated, he or she accurately ascertains the composition of the atmosphere at that place and the condition of the ventilation to determine if it is safe and without risk to persons employed thereat;

(h) where a working place is found to be for the time being dangerous by reason of the presence of gas, instability of roofs, floors or sides or from any other cause, it is so fenced off at each approach as to prevent any person from accidentally entering it and that each fence is clearly marked with an appropriate sign and he or she shall detail the dangers in the general inspection report as specified in Form M5, set out in Schedule 3, provided for the purpose by the operator,

(i) where not less than two means of egress from a working area or from any working place therein are required, forthwith make himself or herself, all persons entering their and all persons assigned to him or her acquainted with two means of egress,

(j) no machinery, apparatus or equipment which is found by him or her, or reported to him or her, to be in an unsafe condition is used while in that condition,

(k) at the end of his or her shift that all places of work where persons in his or her immediate charge are or have been working are left in a safe condition or are fenced off and reported as described in subparagraph (h),

(l) after each shift a written record of the work carried out by all persons under his or her immediate charge and the times of inspection or visits to them is made on the general inspection report as specified in Form M5, set out in Schedule 3, provided for the purpose by the operator,

(m) he or she confers with the oncoming deputy and provides him or her with all relevant information necessary for the safety of persons who will be employed in any working place that he or she had inspected and provide all relevant information necessary for the safety of the persons who will be employed in any working place referred to in the inspection reports required pursuant to these Regulations, and

(n) prior to the commencement of any work confer with the vacating deputy and read inspection reports prepared pursuant to these Regulations that relate to working places where persons in his or her immediate charge may be carrying out work.

Instructions, rules and operating procedures.

19.	The operator shall -

(a)	ensure that suitable instructions and operating procedures are in place at the mine with a view to securing the safe use of work equipment,

(b)	ensure that copies of all instructions, rules and operating procedures required to be made under these Regulations are kept at the mine and given to any person at work at the mine to whom they apply, and

(c)	take all reasonable measures to ensure that each person at work at the mine understands the instructions, rules and operating procedures made under these Regulations that apply to that person.

Permits to work.

20.	The operator shall ensure that -

(a)	based on an assessment of the risks, a system of permits to work is introduced for the carrying out of -

(i)	hazardous activities, and

(ii)	activities which, when carried out in conjunction with other activities, may cause serious risks to the safety, health and welfare of persons at work, and

(b)	a permit to work referred to in paragraph (a) is issued by a competent person before the particular activity concerned commences and specifies the conditions to be fulfilled and protective measures to be taken before, during and after the carrying out of the activity.

Duties of persons at work.

21.	Every person at work to which these Regulations apply shall comply with all applicable instructions, rules, schemes and operating procedures.

Mine safety representative.

22. 	(1) Without prejudice to the provisions of sections 25 and 26 of the Act it shall be the duty of the operator to make and maintain arrangements which will enable him or her and those persons who regularly are employed at the mine to co-operate effectively in promoting and developing measures to ensure the safety, health and welfare of persons who regularly work at the mine and in checking the effectiveness of such measures.

(2)	In accordance with the procedures set out in Schedule 4, the operator shall ensure that there is a mine safety representative at every mine where the number of persons at work at the mine normally exceeds 20.

(3) The operator shall ensure that a mine safety representative, for the purposes of performing functions relating to safety, health and welfare at a mine, has access to –

(a) risk assessments carried out under section 19 of the Act,

(b) information relating to accidents and dangerous occurrences required to be reported under the relevant statutory provisions, and

(c) any information arising from protective and preventive measures taken under the relevant statutory provisions or provided by -

(i) the Authority,

(ii) a person prescribed under section 33 of the Act, or

(iii) a person referred to in section 34(2) of the Act.

(4) The operator shall -

(a) inform the mine safety representative of the time and venue of all mine safety meetings, and

(b) facilitate the attendance of the mine safety representative at mine safety meetings.

Consultation.

23.	Every operator and employer at a mine shall consult at the mine with their safety representatives and employees, as the case may be, in relation to the requirements of these Regulations and section 26 of the Act, taking account of the need, whenever necessary, for co-operation and co-ordination among -

(a)	operators and employers,

(b)	employees and other persons at work, and

(c)	the safety representatives,

in order to promote and develop measures for protecting the safety, health and welfare of persons at work at the mine and to monitor the effectiveness of such measures.

Record keeping.

24.	(1)	The operator shall ensure that -

(a)	every report, notification or other record required to be made under these Regulations is in an approved, or otherwise appropriate, form and kept at the mine or other suitable place, but when mining operations have permanently ceased at the mine the record shall be kept -

(i)	at the registered office of the operator, or

(ii)	where the operator is an individual, at his or her place of business

for a period of 6 years, unless the provision concerned imposes a different period, and

(b)	a copy of the written statement of duties of all persons appointed at the mine under these Regulations is kept at the mine or other suitable place for at least one year from the date of termination of the person’s employment.

(2)	Subject to paragraph (1), where under these Regulations records, reports, or other documents are required to be made, it is sufficient compliance with the requirement if the operator and, where appropriate, other person concerned -

(a)	make and maintain the record, report or other document by electronic means, and

(b)	duly authenticate it as soon as is practicable afterwards.

(3)	Without prejudice to section 64 of the Act, any person having custody of the records required by the Act or these Regulations shall -

(a)	ensure that the records are open to inspection by an inspector, and

(b)	forthwith send to an inspector such extracts from them or copies of them as the inspector may from time to time require in accordance with section 64 of the Act.

PART 3

INSPECTION AND SUPERVISION

Inspection, maintenance and testing schemes.

25.	(1)	The operator shall, with a view to securing, so far as is reasonably practicable, the safety, health and welfare of persons at work in the mine -

(a)	prepare and keep up to date suitable schemes for the systematic inspection, maintenance and, where appropriate, testing of -

(i)	all parts of the mine,

(ii)	all traveling routes, airways, travelways or roads that are not normally places of work,

(iii) 	all shafts and hoisting systems,

(iv)	 all buildings (whether temporary or permanent) at the mine,

(v) 	all electrical installations and circuits at the mine,

(vi) 	any vehicle, plant and work equipment at the mine, and

(vii) 	all equipment provided for fire-fighting at or within the mine.

(b)	ensure that suitable records are made of inspections, maintenance and tests carried out in pursuance of subparagraph (a) and that each such record lists any significant defects and the steps taken, or to be taken by a specified time, to remedy them and is -

(i)	signed by the person making it, and

(ii)	countersigned by an appropriate person in the management structure under Regulation 10, and

(c)	ensure that a sufficient number of competent persons are appointed to undertake the activities referred to in subparagraphs (a) and (b).

(2)	Without prejudice to the generality of subparagraphs (1) (a) and (b), the schemes shall specify that on every working day -

(a) the roofs, floors and sides at every workstation at the mine and every road used by persons at work at the mine for the purpose of their work or of getting to or from their place of work are inspected for loose ground or loose rocks,

(b) all external parts of all machinery and all appliances forming part of the equipment of the mine are inspected, and

(c) where, during an inspection under subparagraph (a), conditions are observed that constitute a significant hazard, or a potential significant hazard, the provisions of Regulation 58 are carried out.

(3)	The operator shall ensure that appropriate remedial measures are taken following an inspection under this Regulation.

(4)	The operator shall ensure that a record is made of each inspection carried out under paragraph (2) and the appropriate remedial measures taken under paragraph (3).

(5)	In this Regulation “inspection” means such visual or more rigorous inspection by a competent person as is appropriate for the purpose.

Supervision of work.

26. 	(1) The operator shall ensure that-

(a) no person passes beyond a meeting station or enters any working area unless instructed to do so by the deputy or supervisor to whom they are assigned unless the person does so in pursuance of an arrangement made by the operator,

(b) no deputy or supervisor instructs any person to enter a working area or go to a working place unless the deputy, supervisor or an authorised competent person is satisfied that it is safe to do so, having regard to any instruction given to the person relating to safety,

(c) a deputy is assigned to each working area for each shift during which any workman is to go into any working place in that area,

(d) subparagraph (c) shall not apply where no persons other than pump-minders, mechanics, electricians, surveyors, engineers or persons performing duties of a specialised nature are working below ground, but the operator shall make suitable arrangements to ensure that the safety of the persons so working is not prejudiced,

(e) the arrangements required to be made by the operator under subparagraph (d) shall be in accordance with at least one of the following provisions, that is to say, any of the persons working below ground shall be:

(i) accompanied at all times during the shift by a competent person appointed by the operator; or

(ii) visited at intervals not exceeding two hours during the shift by an assigned deputy or a competent person appointed by the operator; or

(iii) in telephonic communication at least once in every two hours during the shift, with a competent person appointed by the operator on the surface of the mine, or

(iv) monitored electronically as to their exact location.

Pre-shift inspections.

27.	 The operator shall ensure that -

(a) within two hours immediately before the commencement of work in any working area in the mine, the deputy inspects or causes to be inspected by a competent person, each working place where persons under his immediate charge will be carrying out operations, in order to ascertain -

(i) the adequacy of ventilation,

(ii) the presence of toxic gases,

(iii) the stability of roofs, floors and sides, and

(iv) general safety.

to determine if it is safe and without risk to persons who are to be employed thereat, save that where continuous working is being carried on in that working area the last inspection of the deputy of the previous shift shall be sufficient for such pre-shift inspection if made at intervals not exceeding twelve hours,

(b) where a working place inspected pursuant to paragraph (a) is found to be for the time being dangerous by reason of the presence of gas, instability of roofs, floors and sides or from any other cause, it is so fenced off at each approach as to prevent any person from accidentally entering it and that each fence is clearly marked with an appropriate sign,

(c) the deputy carrying out inspections of each working area shall complete a report of his or her inspection and where they have had cause to have the inspection carried out by a competent person they shall confer with that competent person and complete a report giving the findings and the name of the competent person carrying out the inspection as specified in Form M4 set out in Schedule 3, provided for the purpose by the operator,

Inspections during shifts.

28. 	The operator shall ensure that-

(a) each deputy, at periods not exceeding every four hours, inspects every part of his or her working area required to be ventilated and all workplaces where persons under his immediate charge are carrying out operations, to ascertain the adequacy of ventilation, the presence of toxic gases and the stability of roofs, floors and sides, to determine if it is safe and without risk to persons who are to be employed thereat,

(b) where a working place inspected pursuant to paragraph (a) is found to be for the time being dangerous by reason of the presence of gas, instability of roofs, floors and sides or from any other cause, it is so fenced off at each approach as to prevent any person from accidentally entering it and that each fence is clearly marked with an appropriate sign,

(c) each deputy, within one hour of reaching the surface completes a report of each inspection he or she has carried out and details the findings of each inspection in the general inspection report as specified in Form M5 set out in Schedule 3, provided for the purpose by the operator, and

(d) no duty is assigned to a deputy that would prevent the deputy carrying out his or her statutory duties.

(e) other competent officials, engineers or technicians at periods not exceeding 7 days, inspect every part of the mine where persons regularly pass and every walkable airway, travelway or road not within the working areas of deputies of the mine, to ascertain the adequacy of ventilation, the presence of toxic gases and the stability of roofs, floors and sides, to determine if it is safe and without risk to persons who are to be employed thereat, and

(f) on completion of such inspection specified in subparagraph (e) such competent officials, engineers or technicians complete a report provided for the purpose giving the findings and the name of the competent person carrying out the inspection as specified in Form M6 set out in Schedule 3.

PART 4

ROADS AND VEHICLES

Construction and equipment of vehicles.

29.	The Operator shall ensure that-

(a) every mechanically propelled vehicle in which the motive power is generated by an internal combustion engine is constructed so that air entering the engine is cleaned, the exhaust gases are cooled (where necessary) and diluted and the emission of flame or sparks from the vehicle is prevented,

(b) the battery housing of every mechanically propelled vehicle in which the motive power is generated by an electric motor supplied from a storage battery is adequately ventilated and robustly constructed,

(c) every mechanically propelled vehicle is provided with;

(i) efficient braking systems,

(ii) suitable instrumentation, including adequate warning systems, and a speed indicator placed that can be clearly seen by the driver of the vehicle,

(iii) an audible warning device,

(iv) an efficient lighting system including a head and tail light,

(v) where practicable a cab providing ROPS and FOPS protection,

(vi) an automatic or semi-automatic fire fighting system,

(vii) suitable and sufficient portable fire extinguishers, and

(viii) as appropriate, auxiliary devices as specified in Schedule 5 installed to improve the drivers all round visibility.

Inspection and maintenance of vehicles.

30.	(1) Without prejudice to Regulation 25 the operator shall ensure that-

(a) a system of driver pre-start checking for each mechanically propelled vehicle is operated and maintained to ascertain that it is safe for use,

(b) at least once in every 24 hours each mechanically propelled vehicle is inspected and externally examined by a competent person appointed by the operator, to ascertain that it is safe for use,

(c) at least once in every seven days each mechanically propelled vehicle is inspected and examined, including examination and testing of the braking system, by a competent person appointed by the operator to ascertain that the vehicle is in all respects properly maintained and in good working order,

(d) all defects identified on any mechanically propelled vehicle in relation to subparagraphs (a) to (c), which may be prejudicial to the safety of persons at work are remedied by a competent person before that vehicle is put into service or returned to service, and

(g) the persons referred to at subparagraph (a) to (d) above make true and accurate reports of every such inspection, examination or repair forthwith.

(2) The operator shall ensure that, suitable written reports, are made of inspections, maintenance and tests carried out in pursuance of paragraph (1) and that each report records any significant defects and the steps taken, or to be taken, to remedy them, and

(a) is signed by the person making it, and

(b) countersigned by an appropriate person in the management structure.

(3) The operator shall ensure that a sufficient number of competent persons are appointed to undertake the activities referred to in paragraphs (1) and (2).

Appointment of drivers.

31.	The operator shall ensure that-

(a) all persons in control of mechanically propelled vehicles have been adequately trained in the safe and correct use of such vehicles and are appointed for that purpose in writing, and every such appointment shall be recorded as specified in Form M3 set out in Schedule 2 and shall state the types or classes of vehicles for which the appointment is valid,

(b) only competent and authorised persons drive any mechanically propelled vehicles, except where a person is receiving instruction or training under the direct supervision of a competent and authorised driver or is a person involved in repairing or testing the vehicle,

(c) drivers of mechanically propelled vehicles have received suitable training and re-training in the safe operation of each type of vehicle and any associated equipment they operate, and

(d) no person under the age of eighteen years is permitted to be in control of any mechanically propelled vehicle at the mine.

Carrying of passengers.

32. 	The operator shall ensure that the carrying of passengers on any mechanically propelled vehicle is prohibited other than when-

(a) the vehicle is designed for the carrying of passengers, or

(b) a person providing instruction or training requires the vehicle to be moved in relation to such instruction and training, or

(c) a person repairing or testing the vehicle requires the vehicle to be moved in relation to such repair or testing of the vehicle.

Road surfaces.

33.	The operator shall ensure, so far is reasonably practicable, that the surface and camber of every road used by mechanically propelled vehicles is maintained throughout its length in a condition which is both suitable and sufficient to prevent danger to drivers or pedestrians (or both).

Roadway clearances.

34.	The operator shall ensure, so far as is reasonably practicable, that –

(a) any mechanically propelled vehicle is not used in any road where, after allowing  for the swing of the vehicle, the clearances are not adequate to ensure the safety of the driver, and

(b) where other vehicles or pedestrians (or both) pass, the clearances are not adequate to ensure the safety of other vehicle drivers and pedestrians.

Gradients.

35.	The operator shall ensure that a mechanically propelled vehicle shall not be used on any road where the gradient of any length of road exceeds the maximum gradient specified by the manufacturer of the vehicle.

Safety of pedestrians in roadways.

36. 	The operator shall ensure that-

(a) where pedestrians and mechanically propelled vehicles are present in the same roadway, that preventive measures are taken to minimise the risks to pedestrians traveling that roadway, including where necessary the provision of refuge holes,

(b) where a mechanically propelled vehicle is operated remotely by the driver -

(i) the driver operates the remote control mechanism from a position of safety outside of the expected area of movement of the vehicle, and

(ii) has a clear and unobstructed view of the operations being carried out remotely.

Vehicle and traffic rules.

37.	(1)	The operator shall make suitable vehicle and traffic rules in order to prevent, so far as is reasonably practicable, the risks to persons arising from the use of vehicles at the mine, including where machines or vehicles enter or leave the mine.

(2)	The operator shall ensure that transport vehicles, earth-moving machinery, materials-handling machinery and locomotives used at the mine, including those operated by another employer at the mine -

(a)	are of good design and construction taking into account as far as possible ergonomic principles,

(b)	are maintained in good working order,

(c)	are properly used,

(d)	are not operated otherwise than by -

(i)	a competent authorised person who has attained the age of 18 years, or

(ii)	a person over 17 years who is under the close personal supervision of a competent person for the purpose of his or her training, and

(e)	have, as appropriate, auxiliary devices as specified in Schedule 5 installed 	to improve visibility.

Safeguarding edges of excavations and lagoons.

38.	The operator -

(a)	shall ensure that material is not placed or stacked at the mine near the edge of any excavation or lagoon, where it is likely to endanger persons at work,

(b)	shall not at the mine -

(i)	place or move, or

(ii)	allow to be placed or moved,

any load, vehicle, plant or equipment near the edge of any excavation or lagoon where it is likely to enter the excavation or lagoon or cause a collapse of the side of the excavation or lagoon and thereby endanger any person at work, and

(c)	where necessary, shall ensure that appropriate barriers are provided.

Danger areas.

39.	(1)	The operator shall ensure that -

(a)	danger areas are clearly marked,

(b)	equipment or barriers are installed at all access points of any danger area to restrict inadvertent entry to that area by persons at work not authorised to enter, and

(c)	where a person at work is authorised to enter a danger area, appropriate measures are taken to protect his or her safety, health and welfare.

(2)	In this Regulation “danger area” means an area of the mine at which there is a significant risk to the safety, health or welfare of persons working there, due to the nature of the work being carried out there (including a risk of a person falling a distance likely to cause personal injury) or for any other reason.

Traffic routes.

40.	The operator shall ensure that -

(a)	traffic routes, including stairs, fixed ladders, loading bays and ramps, are designed, located, laid out and made negotiable to ensure easy, safe and appropriate access in such a way as not to endanger persons working in the vicinity of these traffic routes,

(b)	routes used for pedestrian or goods traffic, or both, including those used for loading and unloading, are dimensioned in accordance with the number of potential users and the type of activity concerned,

(c)	if means of transport are used on traffic routes, a sufficient safety clearance or adequate protective devices are provided for other mine users, and routes are clearly marked, regularly checked and properly maintained,

(d)	sufficient clearance is allowed between vehicle traffic routes and doors, gates, passages for pedestrians, corridors and staircases, and

(e)	traffic routes are clearly identified for the protection of persons at work.

Outdoor workstations.

41.	The operator shall ensure that -

(a)	workstations, traffic routes and other areas or installations outdoors that are occupied or used by persons at work in the course of their activities are organised in such a way that pedestrians and vehicles can circulate safely, and

(b)	when persons at work are deployed at outdoor workstations, such workstations are arranged so that they, as far as possible -

(i)	are protected against inclement weather conditions,

(ii)	are not exposed to harmful noise levels or to harmful external influences such as gases, vapours or dust, and

(iii)	cannot slip or fall.

Protection from falling objects and provision of safety helmets.

42.	(1)	The operator shall ensure that -

(a)	adequate measures are taken to prevent persons at work from being struck by any falling object,

(b)	where feasible, persons are protected by collective methods against falling objects, and

(c)	materials, equipment and other articles are laid out or stacked in such a way as to prevent their collapsing or overturning.

(2)	The operator shall ensure that every person under his or her direct control at work at the mine is provided with -

(a)	a suitable safety helmet, or

(b)	other appropriate head protection,

that complies with the relevant statutory provisions, unless there is no foreseeable risk of injury to the head.

(3)	The operator shall ensure that -

(a)	each safety helmet or other head protection provided for use at the mine is marked so that it may be identified by the person to whom it has been issued, and

(b)	the helmet or other head protection is not issued to any other person unless and until it has been cleaned and disinfected.

(4)	A person shall not, at a mine, throw, drop or allow to be shot or ejected downwards any material or object, including waste material, from a height where it is liable to cause injury.

(5)	A person who moves materials or objects, including waste materials, from a height at a mine where they are liable to cause injury, shall lower them so as to avoid injury to persons.

Prevention of drowning.

43.	(1)	The operator shall ensure that where, at a mine, there is a risk of a fall from -

(a)	an edge adjacent to water,

(b)	a structure adjacent to or above water, or

(c)	a floating platform,

secure fencing is provided near the edge, structure or platform, as appropriate, to prevent such a fall.

(2)	To the extent necessary for the access of persons or movement of

materials, paragraph (1) does not apply if  appropriate precautions are taken, so far as is reasonably practicable, to ensure the safety and health of persons at work.

(3)	Without prejudice to paragraph (1), where, in or adjacent to the mine, there is water into which a person, in the course of his or her work, is liable to fall with risk of drowning, the operator shall ensure that -

(a)	suitable rescue equipment is provided, properly maintained and ready for use,

(b)	arrangements are made for the prompt rescue of any such person who is in danger of drowning, and

(c)	personal flotation devices conforming to European Norm (EN) or, where appropriate, an equivalent standard, are provided and worn at all times by persons at risk at the mine.

(4)	The operator shall ensure that personal flotation devices provided under this Regulation are -

(a)	properly maintained,

(b)	checked before each use,

(c)	inspected in accordance with the manufacturer’s instructions, and

(d)	subjected to a thorough examination by a competent person every 12 months.

(5)	On the day of an inspection or examination under paragraph (4), the person who carries out the inspection or examination, as the case may be, shall -

(a)	make a report of the results in an approved form,

(b)	sign and date the report, and

(c)	give a copy of the report to the operator.

PART 5

VENTILATION

# Duty to provide adequate ventilation

44.  (1)	 The operator shall, so far as is reasonably practicable, ensure that-

(a) adequate ventilation is constantly produced in all underground parts of the mine where people are working, traveling through going to or from their place of work, or may have cause to enter in connection with their work, that is sufficient so that -

(i) the atmosphere contains a sufficiency of oxygen,

(ii) any noxious or flammable gases are diluted so as to render them harmless,

(iii) working conditions are reasonable as regards temperature and humidity, and

(iv) occupational exposure limit values applicable for the purposes of the Safety, Health and Welfare at Work (Chemical Agents) Regulations 2001 (S.I. No 619 of 2001) are complied with,

(b) where he or she is temporarily unable to comply with the requirements of paragraph (1)(a) as a result of an interruption to the ventilation, that access to that part of the mine shall be restricted so as to prevent access, other than for the purpose of restoring the ventilation or in case of an emergency, and any persons employed in that part of the mine shall be withdrawn,

(c) in the event of an interruption in the main ventilation supply due to an unscheduled fan stoppage, an automatic alarm activates,

(d) persons do not suffer harm to their health from the adverse effects of extremes of heat or cold, and where conditions in any workplace are, or are likely to be, hot and humid -

(i) those persons are provided with training on measures to be taken to avoid any harmful effects from these conditions,

(ii) appropriate additional workplace environmental controls (including ventilation) and monitoring are implemented,

(iii) where the wet bulb temperature exceeds 25 degrees Celsius, an air velocity of not less than 0.5 metres per second is provided and any appropriate action referred to in subparagraph (ii) is implemented, and

(iv) if appropriate, a programme for monitoring the health of employees in the workplace is implemented.

(2) The requirements of paragraph (1)(a) shall not apply to -

(a) any part of a mine that is stopped off or is inaccessible, or

(b) in any waste.

Main ventilation fans.

45.   The operator shall ensure that-

(a) where adequate ventilation  cannot be provided by wholly natural means that there is provided and maintained at the mine adequate mechanically operated apparatus, hereinafter referred to as the “main ventilation fans”, capable of producing an amount of ventilation sufficient to ensure compliance with Regulation 44,

(b) the main ventilation fans are so designed that the direction of air flow into or out of the mine may be reversed,

(c) an efficient air-lock is provided and maintained separating the main ventilation fans from the  connecting shaft, decline or roadway, and

(d) the depression of the main ventilation fans is continuously monitored and an automatic alarm indicates unscheduled stoppages.

Additional underground fans .

46.	(1) The operator shall ensure that no additional underground fan, other than an auxiliary fan, is installed underground unless -

(a) the additional fan is necessary to ensure compliance with Regulation 44,

(b) a survey of the ventilation of every part of the mine which may be affected by the additional underground fan is undertaken, and

(c) a report is prepared determining the appropriate type, size and location of the additional underground fan.

(2) The operator shall ensure that a record of the survey and report is kept.

# Auxiliary ventilation.

47.	(1)  The operator shall ensure that-

(a) at all working places in the mine, that cannot be adequately ventilated either naturally or by the provision of a main ventilation fan or an additional underground fan, auxiliary ventilation is provided to that place of work,

(b) any auxiliary fan referred to in subparagraph (a) installed at a mine to provide ventilation to working places is -

(i) connected to earth so as to prevent the accumulation of an electro-static charge,

(ii) connected to ducting for conducting air to or from the working place to be ventilated to ensure adequate delivery of air within 5 metres of the furthermost working point,

(iii) installed at a point at a mine not less than 5 metres from the entrance to the place it is to ventilate,

(iv) when forcing ventilation it is installed on the intake side of the entrance, and

(v) when exhausting ventilation it is installed on the return side of the entrance.

(2) The operator shall ensure that -

(a) the quantity of air reaching the auxiliary fan is sufficient to ensure that it does not re-circulate air, and

(b) air circulated by the auxiliary fan referred to in subparagraph (a) is not at any time contaminated by a substantial quantity of any noxious or flammable gas or dust.

(3) The operator shall ensure that a worker shall not enter nor remain in any place in a mine ventilated by an auxiliary fan while the fan is not operating, unless the interruption is temporary and work is ongoing to re-start the auxiliary ventilation.

Prevention of leakage.

48.    The operator shall ensure, so far as is reasonably practicable, that-

(a) measures are in place to prevent leakage of ventilation from intake roadways to return roadways other than where such leakage is planned within the ventilation rules, and

(b) measures are in place to minimise leakage of ventilation into areas of the mine where mining operations are for the time being suspended or complete.

Ventilation rules.

49.   (1) The operator shall cause to be prepared at the mine specific rules, hereinafter referred to as the “ventilation rules” and the ventilation rules shall be reviewed and updated as the development and operation of the mine progresses.

(2) The operator shall ensure that the ventilation rules referred to in paragraph (1) contain -

(a) the minimum quantity of air to be delivered to each working area and working place,

(b) the minimum quantity of air in each intake and return roadway,

(c) the minimum quantity of air to be delivered or exhausted at the end of an air duct attached to an auxiliary fan,

(d) the points within the mine at which the quantity of air passing these points are to be measured and the frequency of these measurements,

(e) the construction of stoppings,

(f) the construction of air-locks, regulators and air doors,

(g) information on the use of brattice sheets, and

(h) the procedures for recording and acting upon the results obtained in the measurements referred to in subparagraph (d).

PART 6

STABILITY AND GROUND SUPPORT

General duty to ensure safety of excavations, tips and lagoons.

50.	The operator shall ensure that excavations, tips and lagoons are designed, constructed (in relation to tips and lagoons), operated and maintained so as to ensure, so far as is reasonably practicable, that instability or movement which is likely to give rise to a risk to the safety, health and welfare of any person is avoided.

Operating procedures for excavations, tips and lagoons.

51.	The operator shall ensure that suitable operating procedures are in place for the safe operation of excavations, tips and lagoons and that such procedures, in particular, specify -

(a)	the manner in which such activities are to be carried out,

(b)	the nature and extent of supervision of such activities, and

(c)	the protective measures to be taken during such activities to ensure the safety, health and welfare of any person and the safety and stability of the excavation, tip or lagoon.

Stability of roads and working places.

52.    The operator shall, so far as is reasonably practicable, ensure that-

(a) all practicable steps are taken to secure the stability of roofs, floors and sides of every travelling road, outlet and working place in a mine and that no person, unless engaged in repairing or in investigating the safety of the workings, travels on or works in any travelling road or working place which is not made secure,

(b) adequate steps are taken by way of controlling movement of the strata in the mine and, where necessary, the implementation of systems for supporting the roof and sides of every road or working place to keep them secure, and

(c) all information relevant to the support of roads and working places in the mine is provided to those affected.

Duty of persons at work in a mine.

53. 	It shall be the duty of every person in the mine to inspect their place of work including access to and egress from the place of work in relation to the condition and stability of roofs, floors and sides and, where necessary, to take appropriate action to make the place safe or, if necessary, to prevent access to that place.

# Scaling of roof and sides.

54. 	It shall be the duty of the operator to ensure that-

(a) appropriate equipment and tools are provided to enable, where necessary, the scaling and dressing of all roads and places of work,

(b) where practicable, primary scaling and dressing is carried out by mechanical means, and

(c) procedures are in place so that any manual scaling and dressing of roads and working places is carried out by persons from a position of safety.

Working at or near unsupported stopes.

55. 	It shall be the duty of the operator to ensure that-

(a) any work at or near any unsupported stope is carried out in such a way that persons are not placed at risk of being struck by falls, slips or movement of ground,

(b) entry to unsupported stopes is controlled and restricted to those carrying out work thereat, operating remotely controlled equipment or equipment provided with a FOPS cab or canopy, and

(c) when work is not being carried out that unintentional entry to that area is prevented by means of a suitable barrier.

The use of backfill material as a means of support.

56.	The operator shall ensure that where the use of backfilling of open areas of the mine forms part of the overall support of the mine-

(a) the area to be backfilled is filled as soon as is reasonably practicable,

(b) the backfill material is placed as tight as is reasonably practicable to the roof and sides of the area being filled, and

(c) adequate measures are taken to prevent the backfill material from migrating from the area being so filled.

Ground support rules.

57.	(1) The operator shall cause to be prepared at the mine specific rules, hereinafter referred to as the “support rules” and the support rules shall be reviewed as the development and operation of the mine progresses.

(2)The support rules referred to in paragraph (1) shall, at a minimum, contain -

(a) details of mine design criteria and the geotechnical properties of strata in the mine,

(b) design criteria for support systems used in the mine,

(c) information and instruction on securing the roof and sides of roads and working places,

(d) a scheme for the inspection of all roads and working places in relation to support,

(e) procedures for mechanical and manual scaling and dressing of roads and working places,

(f) where applicable, measures to determine the solidity of backfill material,

(g) measures taken to monitor the movement of strata within the mine, and

(h) procedures for the evaluation and review of these support rules following incidents of falls, slips or movement of ground.

Appraisal and site investigation of excavations, tips and lagoons.

58.	(1)	Subject to paragraph (2), the operator shall ensure that, before operations commence or re-commence in a particular area in the mine, a suitable geotechnical appraisal of all proposed and existing -

(a)	excavations (including mine faces),

(b)	tips, and

(c)	lagoons

in that particular area is undertaken by a competent person in order to determine whether any such excavation, tip or lagoon represents a significant hazard, or a potential significant hazard.

(2)	Where an appraisal by a competent person under paragraph (1) identifies a significant hazard that cannot be rectified immediately in a safe manner, the operator shall ensure that the provisions of paragraph (4) are complied with.

(3)	Where an appraisal by a competent person under paragraph (1) identifies a potential significant hazard that cannot be rectified immediately in a safe manner, the operator shall ensure that -

(a)	the provisions of paragraph (4)(a) and (b) are complied with, and

(b)	a geotechnical specialist carries out a site investigation to determine whether a geotechnical assessment under Regulation 59 is required.

(4)	Where the conclusion reached by the geotechnical specialist, following a site investigation made under this Regulation, is that the excavation, tip or lagoon represents a significant hazard, the operator shall ensure that -

(a)	appropriate protective measures are taken, including informing all persons affected by it,

(b)	only work that can be carried out safely is undertaken at the excavation, tip or lagoon, and

(c)	a geotechnical assessment is carried out in accordance with Regulation 59.

(5)	The operator shall ensure that -

(a)	any significant findings, and

(b)	any conclusions reached and the reasons for those conclusions

made under an appraisal or a site investigation pursuant to this Regulation, are recorded by the competent person or the geotechnical specialist, as the case may be.

Geotechnical assessments.

59.	(1)	In this Part “geotechnical assessment” means an assessment carried out by a geotechnical specialist identifying and assessing all factors liable to affect the stability and safety of a proposed or existing excavation (including mine faces), tip or lagoon and shall include -

(a)	preparation by or under the supervision of the geotechnical specialist or, as appropriate, consideration by the geotechnical specialist of the documents and particulars specified in Schedule 6,

(b)	the conclusions of the geotechnical specialist as to -

(i)	the safety and stability of the existing or proposed excavation, tip or lagoon being assessed, including his or her conclusions as to whether the excavation, tip or lagoon represents a significant hazard by way of instability or movement,

(ii)	whether any remedial works are required in relation to the excavation, tip or lagoon being assessed and the date by which such works should be completed,

(iii)	the date by which the next geotechnical assessment should take place, and

(iv)	where appropriate, any required changes to the operating procedures in respect of the excavation, tip or lagoon.

(2)	The operator shall ensure that -

(a)	any significant findings made during a geotechnical assessment required under Regulation 59, any conclusions reached in accordance with paragraph (1)(b), and the reasons for those conclusions are recorded by the geotechnical specialist undertaking the assessment,

(b)	the geotechnical specialist signs and dates any such record and records his or her professional qualifications thereon,

(c)	(i)	any information available that may be relevant for the purposes of a geotechnical assessment is made available to the geotechnical specialist undertaking that assessment, and

(ii)	sufficient records are kept of the nature, physical properties and location of all strata or accumulated substances or deposited at an excavation, tip or lagoon to enable an accurate assessment of the stability of that excavation, tip or lagoon to be made,

(d)	any remedial works identified during the geotechnical assessment in accordance with paragraph (1)(b)(ii) are undertaken by the date specified or before mining operations are resumed,

(e)	where the conclusion reached by a geotechnical specialist in accordance with paragraph (1)(b) is that there is no significant hazard -

(i)	the geotechnical specialist specifies the frequency with which appraisals under Regulation 59 are to be conducted in the future in order to ensure the continued safety and stability of the excavation, tip or lagoon, and

(ii)	a record of that specification is made by the geotechnical specialist, and

(f)	copies of all geotechnical assessments are kept at the mine for inspection and are retained by the operator for at least 10 years from the date they were made.

PART 7

EXPLOSIVES

Application of Part 7.

60.	This Part shall apply to the storage, transport, use and disposal of explosives and ANBI at a mine.

Appointment of explosives supervisors, shotfirers and storekeepers.

61.	(1)	The operator shall -

(a)	appoint one or more competent persons as explosives supervisors at the mine 	and obtain confirmation of acceptance of such appointments in writing,

(b)	ensure that, at any given time, there is only one person acting as the explosives supervisor at the mine,

(c)	appoint one or more competent persons as shotfirers and trainee shotfirers at the mine,

(d)	appoint, where necessary, one or more competent persons as storekeepers to ensure the safe storage and transport of explosives at the mine, and

(e)	ensure that a record of the appointment at the mine of any explosives supervisor, shotfirer and storekeeper is kept at the mine or some other suitable place for the period of his or her appointment and for 3 years following the termination of his or her appointment.

(2)	Nothing in these Regulations shall prevent a person appointed as mine manager under Regulation 10(1) (a) from being appointed as explosives supervisor or shotfirer, or both, under this Regulation, provided that he or she is competent to discharge those functions.

Scheme of transit for explosives.

62. 	(1) The operator shall -

(a) in respect of the mine or any part thereof, make a scheme for the conveyance of explosives in these Regulations referred to as a “scheme of transit” whereby explosives from any explosives store or from the place of transfer may, and may only, be conveyed in explosives vehicles to one or more specific stations in the mine (in these Regulations referred to as a “reserve station”) or to a working place for immediate use, or from a reserve station to a working place for immediate use, and

(b) the scheme of transit may include provision for the conveyance of detonators to one or more places of storage in the mine (in this Regulation referred to as a “detonator store”) which shall be apart from any reserve station, or to a working place for immediate use.

(c) the scheme of transit may include provision for the conveyance of ANBI from an ANBI store, or place of transfer, to one or more places of storage underground in the mine (in this Regulation referred to as an “ANBI reserve station”).

(2) The operator of the mine shall ensure that the provisions of any scheme of transit for that mine are executed and enforced.

(3) The operator for the purpose of ensuring safety shall ensure that, every scheme of transit contains provisions relating to each of the following matters:

(a) the location, construction and marking of each explosives store, detonator store, ANBI store, reserve station and place of transfer and the custody of any keys thereof,

(b) the type, design and construction of every explosives vehicle and fire-fighting equipment to be provided on any such vehicle conveying explosives or ANBI,

(c) the supervision and precautions to be taken during the loading, transit and unloading of explosives or ANBI vehicles,

(d) the supervision of explosives, ANBI or detonators at their stores or respective reserve stations,

(e) the manner of conveying explosives and detonators to any working place,

(f) the maximum quantity of –

(i) explosive permitted to be at a reserve station,

(ii) detonators permitted to be at a detonator reserve station, and

(iii) ANBI to be in an ANBI reserve station,

at any time respectively, provided the aggregate quantity of explosives permitted at any given time (in such reserve stations and explosives stores), does not exceed the total licensed explosive limit for those explosives stores, where applicable,

(g) the control and issue of explosives from a reserve station and ANBI from an ANBI reserve station and detonators from a detonator reserve station, ensuring that those removed are those that have been there the longest, and

(h) the return of unused explosive to a reserve station and unused detonators to a detonator reserve station or such other places specified in the scheme.

(4) The operator shall ensure that every scheme of transit contains provisions to ensure that the quantity of explosive in the mine which is conveyed in bulk in pursuance of the scheme and is unused at the mine does not at any time exceed the quantity of explosive so conveyed estimated to be required for use in the mine during the period of forty-eight hours immediately following.

(5) A scheme of transit may impose duties and prohibitions on persons employed at the mine and those persons shall comply therewith.

(6) Subject to Regulation 62(3)(f) and (4), the person in charge of the explosive at any reserve station shall ensure that—

(a) any explosive in the reserve station at the end of his or her period of duty is—

(i) in case the mine is not to be worked during the period of fourteen days next following forthwith returned to the explosives store,

(ii) in case the mine is to be worked during such period—

(I) delivered by him to a person appointed to have charge of them during the shift immediately following his period of duty, or

(II) forthwith returned to the explosives store, or

(III) securely locked in the reserve station, and

(b) in case such explosive is locked in the reserve station under subparagraph (a), the key thereof is forthwith—

(i) delivered to a person appointed to have charge of the explosive during the shift immediately following his or her period of duty, or

(ii) deposited in the explosives store.

(7) The mine manager at a mine at which a scheme of transit is in operation shall ensure that a copy thereof is posted and kept posted and in such characters as to be easily seen and read by persons employed in the mine and that a copy thereof is supplied to each explosives supervisor, shot-firer, trainee shot-firer and person in charge of any explosive at any explosives store, reserve station or detonator store.

(8) In this Regulation “explosive” includes a blasting agent.

Storage, transport, use and disposal of explosives or ANBI.

63.	The operator shall ensure that -

(a)	only suitable explosives, ANBI mixing and pumping apparatus, ANFO 	pumping apparatus, and shot-firing apparatus are used at the mine,

(b)	all explosives, blasting agents and detonators are stored in a suitable licensed 	store, licensed under the Act of 1875 (in these Regulations referred to as an “explosives store”),

(c)	the provisions of the European Communities (System for the Identification 	and Traceability of Explosives for Civil Uses) Regulations 2009 (S.I. No. 133 of 2009) are complied with,

(d)	all explosives and ANBI are received and issued at the mine under the control 	of a competent explosives storekeeper,

(e)	so far as is reasonably practicable, all explosives and ANBI are stored, 	transported, used and disposed of safely and securely,

(f)	operations involving the storage, transport, use or disposal of explosives or ANBI are at all times carried out by, or under the close personal supervision of, persons appointed under Regulation 61,

(g)	such facilities and equipment as are necessary to enable shotfiring operations to be carried out safely and securely are provided,

(h)	any vehicle that is provided for use in relation to shotfiring operations is safe for use and so marked during such use as to be readily identifiable from a distance,

(i)	detonators are stored and transported in suitable containers separate from other explosives or ANBI,

(j)	explosives are kept at all times in a locked explosives store, or in a locked reserve station, or under the close supervision of a suitable person, and

(k)	the security requirements of An Garda Siochana, for the storage, (including at reserve stations), transport, use or disposal of explosives or ANBI,  are complied with at all times.

Shotfiring rules.

64.	The operator shall ensure that suitable shotfiring rules are made, kept up to date and complied with. Such rules shall set out procedures for the following:

(a)	all shotfiring operations at the mine,

(b)	the type and length of shotfiring cable to be used and the procedures to 	protect the cable from sources of extraneous electricity,

(c)	the initiating devices to be used and the arrangements for the inspection, 	testing and maintenance of initiating devices,

(d)	appointing explosives supervisors, shotfirers, trainee shotfirers and storekeepers,

(e)	authorising other persons who will be involved with the storage, transport, use or disposal of explosives or ANBI,

(f)	dealing with misfires,

(g)	disposing of surplus explosives, ANBI, detonators, accessories and packaging.

Blast specification.

65.	The operator shall ensure that -

(a)	an adequate written blast specification, including identification of the danger zone based on an assessment of the risks, is prepared by the explosives supervisor for each shotfiring operation at the mine to ensure that, so far as is reasonably practicable, when such shotfiring occurs, it will not give rise to danger, and

(b)	a copy of any relevant information contained in the blast specification referred to in paragraph (a) is given to any person upon whom it imposes duties.

Shotfiring operations.

66.	The operator shall ensure that -

(a)	so far as is reasonably practicable, each shotfiring operation is carried out safely and in accordance with the shotfiring rules and blast specification,

(b)	all shotfiring operations are carried out under the close personal supervision of the shotfirer,

(c)	a trainee shotfirer at the mine does not fire shots, except when -

(i)	he or she is under the close personal supervision of a shotfirer, or

(ii)	the operator is satisfied that he or she-

(I)	has completed a suitable period of training,

(II)	has appropriate practical experience, and

(III)	is competent,

and

(d)	records of all shotfiring operations carried out at the mine are kept.

Duties of explosives supervisor and shotfirer.

67.	(1)	The explosives supervisor at the mine shall -

(a)	advise the operator as to the observance of the relevant statutory provisions in relation to the storage, transport, use and disposal of explosives or ANBI at the mine,

(b)	organise and supervise all work involving the storage, transport, use and disposal of explosives or ANBI at the mine,

(c)	based on an assessment of the risks, prepare in writing a blast specification for each shotfiring operation which, so far as is reasonably practicable, shall ensure that, when shotfiring occurs, it will not give rise to danger,

(d)	ensure that, prior to shotfiring operations being carried out, he or she is familiar with the area that may be affected by the shotfiring operations, inspects the face, stope or ground to be blasted and is satisfied that the blast specification is adequate,

(e)	ensure that no person carries out any work in relation to explosives unless they are competent, adequately supervised and instructed to do so,

(f)	ensure that all equipment to be used in shotfiring operations is suitable, safe 	and adequately maintained.

(2) The explosives supervisor and the shotfirer at a mine shall carry out any shotfiring operations in accordance with the shotfiring rules and blast specification.

(3) The explosives supervisor and the shotfirer at the mine shall ensure that-

(a) only implements of copper, wood, fibre or other suitable material are used in opening cases or cartons containing explosives or blasting agents,

(b) before drilling is commenced at a working place in a mine the exposed face has been cleaned and examined for misfires, and that any old sockets and cut off holes have been identified and marked,

(c) drilling and charging operations are not carried on simultaneously at the same working place,

(d) the drill hole diameter is adequate to accommodate the largest explosive cartridge or booster to be used,

(e) explosives cartridges are not violently or forcibly pressed into any shot hole,

(f) shot holes are not charged until they have been thoroughly cleaned out,

(g) shot holes are not overcharged,

(h) shot holes are, where necessary, stemmed with suitable stemming to prevent the explosives being blown out,

(i) no person attempts to pull out a detonator lead from any charged shothole,

(j) no person passes any sentry or any barrier erected to prevent access to a danger zone,

(k) any detonators issued to a shotfirer are contained in a suitable securely fastened detonator case and not removed until immediately before use, and

(l) they carry out centralised blasting, where a number of blasts can be initiated simultaneously, only if a risk assessment indicates it is safe to do so.

(4) Before a shot is fired, a shotfirer shall -

(a) ensure that all unused explosives, ANBI and detonators are removed from the area to be blasted,

(b) ensure that no person is within, or may enter within, the danger zone specified in the blast specification when the shot is being fired,

(c) check the shotfiring system or circuit to ensure that it has been connected correctly,

(d) where electrical or electronic detonators are used, ensure that they have been correctly connected to the shotfiring system or circuit and that the shotfiring system or circuit is tested with an instrument suitable for the purpose,

(e) where appropriate, ensure that the electrical integrity of the shotfiring system or  circuit is such as to make a misfire unlikely, and

(f) ensure that the shot is fired from a safe place.

(5) After a shot is fired, a shotfirer or competent person shall -

(a) ensure that no person enters within the danger zone specified in the blast specification until it is safe to do so,

(b) inspect the blast site to check the result of the blast, the condition of the face, stope or ground for the presence of any excessive sockets,

(c) check for any unexploded explosives in the muck pile and establish whether any misfire has occurred,

(d) report immediately any hazardous conditions or misfires to the explosives supervisor, and

(e) ensure that normal working is resumed only when he or she is satisfied that it is safe to do so.

Misfires.

68.	In the event of a misfire, the explosives supervisor, in consultation with the shotfirer, shall ensure, so far as is reasonably practicable, that -

(a)	no person, other than himself or herself, the shotfirer, any trainee shotfirer or any other person authorised by him or her, enters the danger area -

(i)	where the shot was fired by means of safety fuse, until a period of 30 minutes has elapsed since the misfire, or

(ii)	where the shot was fired by other means, until any shotfiring apparatus has been disconnected from the shot and a period of 5 minutes has elapsed since the misfire,

(b)	appropriate steps are taken to determine the cause of the misfire and to deal with it, and

(c)	a suitable record is kept of the misfire and any action taken.

Prohibited activities.

69.	(1) The operator shall ensure that no person, other than -

(a)	a person authorised for the transport of explosives or ANBI to or from a an explosives store, a reserve station, a place of work or place of transfer,

(b)	an explosives supervisor,

(c)	a shotfirer or trainee shotfirer,

(d)	a storekeeper, or

(e)	any other person authorised by the operator to do so,

shall handle explosives or ANBI  at a mine.

(2) 	The operator shall ensure that no person -

(a) drills any drill holes within 150 millimetres of any old sockets, cut off holes or shothole remnants,

(b) drills any drill holes within 1.5 metres of a hole containing any explosives or blasting agents, and

(c) carries out any drilling and charging operations simultaneously in any working area or on the same face in a mine within 10 metres of each other,

(3) 	The operator shall ensure that no person brings any substance or article (other than explosives) likely to cause an unintended explosion or fire within 100 metres of any explosives or ANBI or (except for the purpose of lighting igniter cord or safety fuse) take any naked flame within 100 metres of any explosives or ANBI at a mine.

(4)	The operator shall ensure that no person shall forcibly remove any detonator lead, safety fuse or other system for initiating shots from a shothole at a mine after the shothole has been charged and primed.

(5)	The operator shall ensure that no person shall charge or fire a shot in a shothole in which a shot has previously been fired, unless he or she is dealing with a misfire in accordance with action taken under Regulation 68.

(6)	The operator shall ensure that no person shall fire a shot at a mine -

(a)	unless he or she is an explosives supervisor, shotfirer or trainee shotfirer within the meaning of these Regulations, and

(b)	other than by means of a suitable exploder, suitable safety fuse or other suitable means provided by the operator.

(7)	The operator shall ensure that no person shall cap a safety fuse with a detonator unless he or she is competent to do so, is using equipment designed for the purpose and he or she is in a suitably sheltered place designated by the operator for the purpose.

(8)	The operator shall ensure that no person, other than an explosives supervisor, explosives storekeeper, shotfirer or trainee shotfirer, shall dispose of surplus explosives, ANBI, detonators, accessories or packaging remaining following shotfiring operations at a mine.

Records of explosives.

70.	(1) The operator shall ensure that procedures are in place for accounting for all explosives and ANBI used at the mine.

(2) The operator shall comply with any requirements of An Garda Siochana regarding such records and accounting.

(3) In accordance with the European Communities (System for the Identification and Traceability of Explosives for Civil Uses) Regulations 2009 (S.I. No 133 of 2009), the operator shall ensure  that records are kept of -

(a) the quantity and unique identification of explosives received at the mine,

(b) the quantity and unique identification of explosives transported to reserve stations,

(c) the quantity and unique identification of explosives issued to each shotfirer or other competent person,

(d) the quantity and unique identification of explosives used in each blast,

(e) the quantity and unique identification of explosives returned to reserve stations or explosive stores, and

(f) the quantity and unique identification of surplus or defective explosives safely disposed of.

(4) All such records in relation to this Regulation shall be kept in accordance with Regulation 24 for a period of 10 years and shall be available for inspection by an inspector or a member of An Garda Siochana on request.

PART 8

ELECTRICITY

General.

71. 	(1) This Part is in addition to and not in substitution for Part 3 of the Principal Regulations.

(2) The operator shall ensure that the entire electrical installation within the mine complies with Part 3 of the Principal Regulations and the provisions of this Part.

Protection of cables.

72. 	The operator shall ensure that all cables conducting electrical energy at potentially dangerous voltages are suitably protected by armouring and positioning as appropriate to reduce as low as reasonably practicable the possibility of inadvertent contact with a live conductor.

Introduction of electrical equipment.

73. 	Before electrical equipment is first introduced into an underground mine, the operator shall prepare or have prepared, and kept available to an inspector, a copy of the ventilation plan, on which the intended locations of that equipment shall be shown, together with a copy of any schematic diagram relating to that part of the mine, prepared in accordance with good practice and for the purposes of Regulation 77.

Restriction of certain categories of electrical equipment in certain zones below ground.

74.	(1) At every underground mine containing zones in which flammable gasses or flammable dusts are potentially present, in quantities sufficient to indicate danger, the operator shall ensure that a suitable plan identifying such zones is prepared.

(2) The operator shall ensure that all electrical equipment in these zones has a certificate of conformity in accordance with the European Communities (Equipment and Protective Systems Intended for Use in Potentially Explosive Atmospheres) Regulations 1999 (S.I. No. 83 of 1999) and be catagorised either as Group I, equipment category M1 or Group II, equipment category M2, as appropriate.

(3) The operator shall ensure that electrical equipment is not energised in such zones unless it is -

(a) equipment of a kind suitable for that purpose  catagorised as Group I, equipment category M1and is,

(b) equipment which is not capable of producing incendive electrical sparks or other source of ignition in  normal use, or

(c) electrically powered equipment not permanently installed in the mine but required occasionally for monitoring, testing, recording and measurement, and used where the concentration of flammable gasses or dusts is lower than that which might cause risk in accordance with suitable rules drawn up by a competent person to ensure that danger will not thereby arise, which rules shall in particular include provision for personal supervision of that equipment by a competent person and testing for flammable gasses when it is in use.

Cutting off electricity or making safe where flammable gasses are found.

75.	(1) Where flammable gasses or dusts are detected in a mine either below ground or on the surface in a concentration giving rise to risk of a dangerous conflagration, the operator shall ensure that a system is in place that-

(a) cuts off the supply of electricity to any electrical equipment situated at the

place where the said concentration was detected,

(b) takes all reasonably practicable steps to make equipment in such a place safe,

except that this paragraph shall not apply if the electrical equipment is suitable for the purpose of remaining energised in such circumstances .

(2) If the supply of electricity to electrical equipment is cut off or the equipment is made safe in accordance with paragraph (1), it shall remain in that condition until a competent person on duty at the mine having determined that it is safe to do so, directs that such precautions are no longer necessary.

(3) If the supply of electricity to electrical equipment is cut off or the equipment is made safe in accordance with paragraph (1), details of the time, duration and location shall be recorded.

Means of cutting off electricity to circuits below ground.

76.	At every mine at which electrical equipment which may give rise to danger is installed below ground and is supplied from a power source at the surface of the mine, the operator shall ensure that switchgear is provided at the surface for cutting off the supply of current to that equipment and that adequate provision is made for the operation of that switchgear, including such means of communication as will, so far as is reasonably practicable, enable the switchgear to be operated in case of danger.

Schematic diagrams.

77.	(1) The operator shall ensure that suitable schematic diagrams and layout drawings  of all electrical distribution systems intended to be operated at the mine (other than those operating at a voltage not exceeding 250 volts) shall, so far as is reasonably practicable —

(a) be prepared and kept in the office at the mine, and

(b) show the planned settings of any circuit electrical protective devices.

(2) Copies of such portions of the schematic diagrams prepared pursuant to paragraph (1) as are necessary to prevent danger and which show at least those parts of the electrical system which are served by switchgear operating at a voltage in excess of 250 volts shall be displayed at each place where such switchgear is installed with the exception of locations of feeders to portable or mobile equipment.

(3) The operator shall ensure that plans on a suitable scale are kept in the office at the mine showing, so far as is reasonably practicable, the position of all permanently installed electrical equipment at the mine.

Electric shock notices.

78.	Where, at any place at a mine, electric arc welding is taking place or electrical energy

is being generated, transformed or used at a nominal voltage in excess of 125 volts a.c. or 250 volts d.c., the operator shall ensure that a notice is displayed in a form which can be easily read and understood and containing information on the appropriate first aid treatment for electric shock and details of the emergency action to be taken in the event of electric shock.

Storage, charging and transfer of electrical storage batteries.

79.	The operator shall ensure that, at any mine in which electrical storage batteries are used below ground, those batteries are, so far as is reasonably practicable, used, stored, charged and transferred in a safe manner.

Leakage protection.

80. 	The operator shall ensure that -

(a) in relation to every circuit in which alternating current at a voltage exceeding 1,000 volts is used, effective means is provided for automatically cutting off the supply of electricity from that circuit, with the leakage trip level set as low as is reasonably practicable, but in any case set no higher than 10 percent of maximum current for which that circuit is designed or 2 amperes, whichever is the greater.

(b) in relation to all circuits supplied at voltages less than 1,000 Volts, a risk assessment is carried out by a competent person to ensure that adequate operational leakage protection is fitted to all appropriate circuits.

Reportable incidents.

81.	The operator shall ensure that, notwithstanding the requirements of Regulations 58 to 62 of the Safety Health and Welfare (General Application) Regulations 1993 (S.I. No. 44 of 1993) all instances where a person reports suffering any electric shock or burn at a mine, from direct or indirect contact with a conductor in an electric circuit (being a circuit in which the voltage for the time being exceeds twenty five volts) is reported, as soon as reasonably practicable, to the Authority.

New installations and major alterations.

82.	(1) Upon the completion of every new installation and every major alteration to an existing installation and without prejudice to Regulation 25, the operator shall ensure the testing by a competent person appointed by him or her of such installation or alteration as regards each of the following, namely;

(a) verification of polarity,

(b) the conductance of the earth conductors and earth plates or earth rods,

(c) the effectiveness of the earth loop impedance,

(d) the effectiveness of every current leakage circuit breaker,

(e) the insulation resistance of every circuit, and

(f) any other aspect of the installation as required by a competent person or an inspector.

(2) Every person who has made a test in pursuance of this Regulation shall record and sign a report of test and inspection containing the particulars specified in paragraph (1).

PART 9

ACCESS, EGRESS AND EMERGENCY PLANNING

Outlets and workings.

83.	 The operator shall ensure that-

(a) all underground workings have access to the surface by at least two separate outlets which are soundly constructed and readily accessible to underground workers,

(b) mechanical man-winding facilities, man-riding facilities or other means of transport are available for the outlets referred to in subparagraph (a), if considerable physical effort is involved in negotiating them, and

(c) roadways are so marked or signposted to enable workers to find their way about the workings.

Ladderways between working levels.

84.	The operator shall ensure that where a mine is worked at more than one level or in more than one seam then connection between each level or seam is provided and accessible at all times by use of ladderways or stairways, notwithstanding the provisions of Regulation 83.

Entrances to shafts, staple pits, ore passes and stopes.

85. 	The operator shall ensure that entrances to shafts, staple pits, ore passes and stopes are -

(a) so protected so as to prevent inadvertent access, and

(b) marked with warning signs in accordance with the relevant statutory provisions applying to safety and health signs at work.

Pedestrian and vehicle traffic routes.

86.	The operator shall ensure that -

(a)	traffic routes, including stairs, fixed ladders, loading bays and ramps, are designed, located, laid out and made negotiable to ensure easy, safe and appropriate access in such a way as not to endanger persons working in the vicinity of these traffic routes,

(b)	routes used for pedestrian or goods traffic, or both, including those used for loading and unloading, are dimensioned in accordance with the number of potential users and the type of activity concerned,

(c)	if means of transport are used on traffic routes, a sufficient safety clearance or adequate protective devices are provided for other quarry users, and routes are clearly marked, regularly checked and properly maintained,

(d)	sufficient clearance is allowed between vehicle traffic routes and doors, gates, passages for pedestrians, corridors and staircases, and

(e)	traffic routes are clearly identified for the protection of persons at work.

Escape and rescue facilities.

87.	Without prejudice to section 11 of the Act, the operator shall ensure that –

(a)	adequate means of escape and rescue are provided and maintained, so as to enable persons to leave the mine promptly and safely in the event of danger,

(b)	adequate means of communication and warning are provided to enable assistance, escape and rescue operations to be launched at once when required,

(c)	instructions concerning the use of emergency equipment and the action to be taken in the event of an emergency at or near the mine are prepared,

(d)	persons at work at the mine are trained in appropriate action to be taken in the event of an emergency,

(e)	rescue equipment is provided, maintained in good working condition and kept ready for use at readily accessible, appropriately sited and clearly sign-posted places,

(f)	emergency routes and exits remain clear and lead by the most direct means to the open air, a safe area or a safe assembly or evacuation point,

(g)	the number, distribution and dimensions of the emergency routes and exits are appropriate to the use, equipment and dimensions of the mine and the maximum number of persons that may be present,

(h)	emergency doors open outwards and are not so locked or fastened that they cannot be easily and immediately opened by any person who may require to use them in an emergency,

(i)	emergency routes and exits, and the traffic routes and doors giving access to such routes and exits, are free from obstruction so that they can be used at any time without hindrance,

(j)	emergency routes and exits requiring illumination are provided with emergency lighting of adequate intensity, and

(k)	specific emergency routes and exits are indicated by signs in accordance with the relevant statutory provisions applying to safety and health signs at work.

Safety drills.

88.	The operator shall ensure that safety drills are held at the mine at regular intervals (at least once per year) for persons at work there for the purposes of -

(a)	training the persons who work at the mine in the appropriate actions to be taken in an emergency, including, where appropriate, the correct use, handling and operation of emergency equipment, and

(b)	training and checking the skills of rescue teams referred to in Regulation 103 and such other persons to whom specific duties involving the use, handling and operation of such equipment have been assigned in the event of an emergency.

Fire and explosion hazards.

89.	(1)	This Regulation applies without prejudice to section 11 of the Act and the Fire Services Acts 1981 and 2003 (No. 30 of 1981 and No.15 of 2003).

(2)	The operator shall ensure that -

(a)	no person at work at the mine uses a naked flame or carries out any work that could give rise to a risk of an unintended fire or explosion, unless sufficient measures to prevent such a fire or explosion are taken, and

(b)	no person smokes or carries a lighted pipe, cigar or cigarette in any part of the mine where there is a risk of fire or explosion.

(3)	The operator, depending on the features of the mine, the dimensions and use of rooms, the on-site equipment, the physical and chemical properties of the substances present and the maximum potential number of persons present at work, shall provide, or cause to be provided, at the mine an adequate number of -

(a)	appropriate fire-fighting devices, and

(b)	where required, fire detectors and alarm systems.

(4)	The operator shall ensure that -

(a)	fire-fighting devices, fire detectors and alarm systems are regularly checked and properly maintained,

(b)	appropriate tests and fire drills take place at regular intervals,

(c)	non-automatic fire-fighting equipment is easily accessible, easy to use and, where necessary, protected from potential damage, and

(d)	fire-fighting equipment is indicated by signs in accordance with the relevant statutory provisions applying to safety and health signs at work.

Explosive or harmful atmospheres.

90.	(1)	Where there is a potential for harmful or explosive atmospheres to be present at the mine, the operator shall ensure that-

(a)	adequate steps are taken in order to determine whether potentially harmful or explosive substances are present in the atmosphere and, where such substances are present, a risk assessment is carried out by a competent person and the concentration of such substances likely to be in the atmosphere is measured at all relevant locations in the mine,

(b)	automatic devices are provided that are designed to -

(i)	monitor continuously the concentration of explosive or flammable gases or dusts in the atmosphere,

(ii)	trigger an alarm if such concentration reaches a dangerous level, and

(iii)	cut off power to any plant that, because of the concentration of such gases in the atmosphere and the nature of the plant, gives rise to a risk to the safety and health of any person,

(c)	where devices are provided in accordance with subparagraph (b)(i), a record of the levels of concentration of such gases in the atmosphere is made at such intervals as are deemed necessary by a competent person and specified in the safety statement.

(d)	at any place in the mine where there is a risk of the occurrence or accumulation of an explosive atmosphere, all necessary measures are taken in order -

(i)	to prevent such occurrence and accumulation, or

(ii)	where this is not practicable, to prevent the ignition of such an atmosphere, and

(e)	at any place in the mine where there is a risk of the occurrence or accumulation of a substance harmful to health in the atmosphere, appropriate measures are taken in order to -

(i)	prevent such occurrence and accumulation or, where this is not practicable,

(ii)	extract or disperse that harmful substance in such a way that persons are not placed at risk.

(2)	When persons at work are present in a particular place in the mine where they are exposed to a substance in the atmosphere that is, or may be, harmful to health, the operator shall ensure that -

(a)	appropriate and sufficient breathing and resuscitation equipment is -

(i)	available,

(ii)	suitably stored, and

(iii)	maintained,

(b)	a sufficient number of persons trained in the use of such equipment are present, and

(c)	where harmful substances accumulate or may accumulate in the atmosphere, appropriate measures are taken to ensure -

(i)	their suppression at source,

(ii)	their extraction at source,

(iii)	their removal, or

(iv)	the dilution of accumulations of such substances, in such a way that persons are not at risk.

Lighting.

91.	The operator shall ensure that -

(a)	the mine is provided where appropriate with lighting capable of supplying illumination sufficient to ensure the health and safety of persons therein,

(b)	workstations, as far as possible -

(i)	receive sufficient natural light, and

(ii)	bearing in mind the climatic conditions, are equipped with artificial lighting adequate for the protection of the safety and health of persons at work,

(c)	lighting installations in rooms containing workstations and in passageways are placed in such a way that the type of lighting provided does not present a risk of accident to persons at work, and

(d)	every part of the mine in which a person is likely to be exposed to risks in the event of the failure of artificial lighting is provided with emergency lighting of adequate intensity and, where that is not possible, persons at work in that place are provided with an appropriate personal lamp.

Prevention of unauthorised entry.

92.	The operator shall ensure that -

(a)	mine boundaries are signposted and laid out so as to be clearly visible and identifiable,

(b)	safe means of access and egress at the mine are -

(i)	provided and maintained, and

(ii)	where appropriate, indicated,

(c)	adequate precautions are taken to protect persons present at, or in the vicinity of, the mine from risks that may arise from mining operations, and

(d)	adequate precautions are taken to prevent unauthorised entry to the mine including, where appropriate, the provision of barriers.

Means of evacuation.

93.	The operator shall ensure that all persons employed underground have received training in the appropriate action to be taken in emergencies.

Underground workforce accounting.

94.	The operator shall ensure that procedures or means are in place so that it is possible at all times to know the numbers and identities of any persons employed underground at any time and their probable location.

Precautions for withdrawal of employees.

95.	The operator shall ensure that-

(a) all persons employed below ground are provided with self-rescue respiratory devices, which are within reach at all times when below ground, so as to enable them to withdraw in safety from the mine or to a place of safety,

(b) all persons employed underground are trained in the use of devices referred to in subparagraph (a) and in maintaining the devices within their reach at all times when below ground, and

(c) devices referred to in subparagraph (a) shall be kept and maintained at the mine to ensure that they are in good condition.

Precautions against external dangers to workings.

96	The operator shall ensure that (a) such steps as may be necessary are taken so that employees are in possession of all information indicating the presence of -

(i) any disused workings, openings or cavities (whether mine workings or not),

(ii) any rock or stratum likely to contain water (whether dispersed or in natural cavities),

(iii) any peat, moss, sand, gravel, silt or other material likely to flow when wet, and the sea, a lake or river or any other body of surface water, and

(iv) any natural feature or disused working that may contain noxious or flammable gas in such quantity and volume as to be a danger to persons employed below ground.

(b) such steps are taken as may be necessary to verify any such information, including the determination of the vertical and horizontal distances of the workings to any of the external dangers, identified in paragraph (a).

(c) arrangements are in place to ensure the safety, health and welfare of persons carrying out work adjacent to, approaching or near to any of the external dangers identified in paragraph (a).

Precautions against the outbreak of fire.

97.	The operator shall ensure that-

(a) the quantity of flammable materials that may be taken into the mine is no more than is necessary for the efficient operation of the mine,

(b) where flammable materials are stored in the mine in significant quantities, procedures are in place to ensure the safety, health and welfare of persons employed in the mine,

(c) where it is necessary to use hydraulic fluids for the transmission of energy, fluids which are difficult to ignite are, as far as possible, used in order to avoid the risk of fire and its spread and such hydraulic fluids satisfy specifications and test conditions relating to fire resistance and hygiene criteria,

(d) where hydraulic fluids are used which do not satisfy the specifications, conditions and criteria referred to in subparagraph (c), additional precautions are taken to avoid the increased risk of fire and its spread,

(e) where cylinders of compressed gas are used below ground, they are installed and maintained with a suitable safety valve, stored in a safe condition and procedures are in place to minimise the risk of the outbreak of fire,

(f) the necessary measures are taken to prevent the formation, accumulation and ignition of explosive atmospheres,

(g) provision is made to prevent fires from starting and from spreading,

(h) provision is made for fast and effective fire-fighting and the adequate supply of fire-fighting materials,

(i) all working places at or within the mine are equipped with appropriate fire-fighting equipment and, as necessary, fire detection and alarm systems, and

(j) non-automatic fire-fighting equipment is easily accessible, simple to use and protected from accidental damage.

Inspection of fire-fighting equipment.

98.	The operator shall ensure that a scheme is prepared for the inspection of all equipment provided for fire-fighting at or within the mine in accordance with Regulation 25.

Warning of emergencies.

99.	The operator shall ensure that-

(a) suitable and efficient means are provided for the purpose of warning and communicating to those employed below ground of any emergency necessitating a speedy evacuation of the workings and to enable assistance, escape and rescue operations to be immediately activated, and

(b) a test of the effectiveness of the warning shall be made at least once a year, and a report of the effectiveness and of any necessary remedial action required to be taken in respect of any test carried out is forwarded to the authority within 30 days of the carrying out of the test.

Refuge stations.

100.	The operator shall ensure that-

(a) a sufficient number of refuge stations are provided below ground at the mine at locations close to work places where evacuation to the surface in an emergency situation may not be possible or may place persons at undue risk,

(b) any refuge stations provided in relation to subparagraph (a) are so designed that any gases, fumes, or products of combustion are prevented from entering,

(c) any refuge station provided in relation to subparagraph (a) is of suitable size and dimensions for the number of persons that may be required to enter it, and

(d) any refuge station provided in relation to subparagraph (a) is provided with a supply of potable water, equipment for maintaining a respirable atmosphere and, where practicable, a means of communication.

Rescue teams.

101. 	(1) The operator shall ensure, so far as is reasonably practicable, the organisation and maintenance of rescue teams at a mine as follows-

(a) where the number of persons employed below ground in the mine does not exceed one hundred, at least one team,

(b) where the number of persons employed below ground in the mine exceeds one hundred but does not exceed three hundred and fifty, at least two teams, or

(c) where the total number of persons so employed in the mine exceeds three hundred and fifty, at least 3 teams.

(2) The requirement in paragraph (1) (a) shall not apply where risk assessment indicates that the provision of a rescue team is unnecessary or where arrangements are in place whereby a team from another mine will be made promptly available in case of need.

(3) Where a number of mines operate within a five mile radius, they may, upon agreement with the operators of each of the mines, be treated together as a single mine for the purpose of this Regulation.

Composition of rescue teams.

102.	The operator shall ensure that each rescue team formed pursuant to Regulation101-

(a) comprises not less than five persons employed at the mine that are fully trained in rescue work,

(b) has a competent person appointed to be the captain of rescue team,

(c) comprises of persons who have undergone a thorough medical examination by a registered medical practitioner to ensure that they are physically fit and fit also to undertake strenuous rescue work and so certified in Form M7 set out in Schedule 9,

(d) comprises of persons with two years or more underground mining experience in operations at that mine or a mine using similar working methods,

(e) is not employed below ground simultaneously, otherwise than in rescue work or practice, and

(f) are provided with communication devices so that they can be summoned to the mine in an emergency at times when they are not employed at the mine.

Training of rescue workers.

103.	The operator shall ensure that every member of a rescue team-

(a) has attended one or more courses of instruction and practice, being courses complying with the initial training scheme for rescue work specified in  Schedule 2,

(b) has been certified by an instructor as being trained and competent in the use of breathing apparatus for rescue work,

(c) holds a certificate in first–aid issued within the immediately preceding three years by a person recognised as an occupational first-aider by an approved person as required by Regulation 163 of the Principal Regulations,

(d) has been certified within the last 12 months by a registered medical practitioner following a thorough medical examination to be physically fit and fit to undertake strenuous rescue work, and

(e) has attended a course of instruction and practice in rescue work as described in Schedule 2.

Equipment to be provided for rescue work.

104.	(1) The operator shall ensure that for rescue work there shall be provided and maintained in readiness for immediate use at the mine-

(a) sufficient, suitable and complete sets of breathing apparatus,

(b) suitable equipment for charging and re-charging of the breathing apparatus,

(c) a sufficient and suitable number of smoke helmets and ancillary equipment,

(d) sufficient and suitable reviving apparatus,

(e) suitable and sufficient first–aid equipment for rescue work,

(f) sufficient electric safety lamps,

(g) suitable and sufficient devices for making immediate determinations of the atmosphere and the presence and concentrations of noxious or toxic gases, and

(h) suitable and sufficient communication and signaling devices.

(2) The operator shall ensure that equipment required to be provided under paragraph (1) is kept at the mine at a place not used for any other purpose.

(3) The operator shall provide near to the shaft or outlets an adequately heated, lit and properly maintained accommodation for persons engaged in rescue work or practice.

(4) The requirements of paragraphs (1) and (2) shall not apply to mines to which Regulation 101(2) and (3) apply.

Fresh air base.

105.  The operator shall ensure that-

(a) the captain of a rescue team before rescue work or training for rescue work is undertaken establishes a forward control point, hereinafter referred to as the “fresh air base”, being a place where breathing apparatus can be donned or removed and other operations undertaken in a safe-air environment,

(b) the captain of a rescue team does not proceed beyond the fresh air base without a plan of the relevant part of the mine, communication and agreement with the incident controller on the route to be taken and the time estimated to reach the danger area or search area,

(c) the captain of a rescue team engaged in rescue work or training for rescue work in any mine devotes himself to the direction of the rescue team and to secure to the best of his or her ability the team safety, and

(d) during rescue work and rescue work training an effective system of communication is established between;

(i) the incident controller and the fresh air base,

(ii) members of the team itself, and

(iii) any rescue team and the fresh air base.

Rescue plans.

106.	The operator shall ensure that a plan, or set of plans, is kept at the mine and brought up to date, where necessary, at least every three months in a form suitable for use by rescue workers, of the workings of the mine showing clearly and accurately –

(a) the extent of the workings,

(b) the airways,

(c) the direction of the air current in each roadway,

(d) all principal doors,

(e) stoppings,

(f) air-crossings,

(g) regulators,

(h) refuge stations,

(i) first-aid points,

(j) fire-fighting points, and

(k) telephone points.

Incident controller.

107.	The operator shall ensure that a competent person, or persons, at the mine is appointed to act as incident controllers so that one of them takes charge on the surface at all times when rescue work is being undertaken and that they co-ordinate and facilitate the rescue work and ensure that persons necessary for providing assistance to the rescue team are available.

Emergency procedures.

108.	(1)	The operator shall, in accordance with Section 11 of the Act, prepare emergency rules and procedures hereinafter referred to as the “emergency procedures” and these procedures shall include-

(a) situations and scenarios when the emergency procedures may be require to be invoked,

(b) the procedure for reporting an occurrence that may invoke the emergency procedures,

(c) procedures to be followed by persons employed below ground when the emergency procedures are activated,

(d) means for communicating an emergency situation to persons employed below ground,

(e) procedures for notifying and assembling rescue teams,

(f) procedures for accounting for persons within the mine,

(g) restrictions on entry of persons into the mine, or parts of the mine, during an emergency,

(h) duties of incident controllers and other persons having duties in an emergency, not directly related to rescue work,

(i) duties of rescue team captains to their team,

(j) duties of rescue workers,

(k) procedures for notifying the relevant authorities, and

(l) procedures for declaring the emergency over.

(2) The requirements of Section 19 of the Act, shall not apply to persons engaged in rescue work where such activity prevents compliance with that section.

PART 10

PREPARATION OF MINE PLANS

Appointment and qualifications of mine surveyor.

109.	The operator shall appoint a competent person (hereinafter referred to as the “surveyor”) to be the surveyor for the mine holding an acceptable qualification in surveying and membership of a professional body.

Duties of the mine surveyor.

110.	The operator shall ensure that the surveyor-

(a) prepares or supervises the preparation of all plans, drawings and sections, including all working plans, ventilation plans, and rescue plans,

(b) ensures the accuracy of any plans, drawings and sections prepared in relation to paragraph (a),

(c) keeps all working papers recording observations and calculations which were necessary for the preparation or checking of any plans, drawings and sections prepared in relation to paragraph (a),

(d) where necessary, revises any plans, drawings and sections prepared in relation to paragraph (a) at a period not exceeding three months, and

(e) ensures upon his or her ceasing to be the surveyor for the mine or upon the abandonment of the mine that a complete set of such plans, drawings, sections and working papers are transferred to the operator.

Scale, datum and other details required on plans.

111.	The operator shall ensure that the surveyor  in preparing working, ventilation and rescue plans pursuant to Regulation 110, ensures that such plans, drawings and sections –

(a) (i) are to a scale not less than 1/2,500,

(ii) are oriented to and correlated with the Ordnance Survey National Grid and marked with kilometre squares.

(b) indicate variations in level from an assumed datum below ordnance datum -

(i) on every main intake or return airway,

(ii) so far as can be ascertained, on the outline of any disused or abandoned workings shown on the plan, and

(iii) at horizontal intervals not exceeding 100 metres.

(c) indicate the position of any workings which are not disused or abandoned up to a date not more than 3 months past,

(d) indicate the position of any workings which are disused and abandoned inside the mining boundary or within 100 metres of the boundary in a straight line in any plane and less than 40 metres above the boundary that may contain an accumulation of water dangerous to persons working in the mine,

(e) indicate any workings of any other mine, whether abandoned or not, within 100 metres of the boundary in a straight line in any plane and less than 40 metres above the boundary that may contain an accumulation of water dangerous to persons working in the mine,

(f) indicate, within 40 metres of any working in a mine or within 100 metres of the boundary of any mine-

(i) any rock or stratum containing or likely to contain water, whether dispersed or in natural cavities, which might constitute a danger to persons at the mine, and

(ii) any peat, moss, sand, gravel, silt or other material that is likely to flow when wet are marked with contour lines indicating the level of the floor of the workings being worked from an assumed data below ordnance datum,

(g) indicate the position, direction, extent and vertical throw, so far as they can be ascertained, of any known fault , washout, roll, igneous intrusion or other displacement in the strata,

(h) where more than one seam, vein, lode or level is worked that plans are prepared for each seam, vein, lode or level showing clearly and accurately the workings and the position of all shafts, outlets, drifts or staple pits at that level or within 40 metres above or below that level,

(i) show the direction of the National Grid North,

(j) state the date and by whom it was prepared.

Additional plans.

112. 	The operator shall ensure that in addition to the plans, drawings and sections required to be prepared pursuant to Regulation 110 the surveyor prepares or has prepared the following-

(a) a plan showing the system of ventilation in the mine and in particular the general direction of the flow of ventilation, the points at which the quantity of air passing is required to be measured under the mine ventilation rules and the principal devices for regulating the flow of ventilation and indicating intake airways in blue and return airways in red,

(b) a sketch plan of the mine showing the main roads and means of access and egress from each part of the mine to the surface,

(c) a geological map showing the boundaries of the mine workings, the geology of strata and occurrence of any superficial and drift deposits,

(d) a section of the geological strata passed through by any shaft, outlet , drift or staple pit, and

(e) in the event of the abandonment of a mine, seam, vein, lode or level, an abandonment plan, including drawings and sections to indicate the final position of mine workings in that mine, seam, vein, lode or level and the position of any item required to be indicated on the working plan and of the position, size and dimensions of any stopping, seal or dam erected to prevent entry.

Keeping of plans.

113. 	The operator shall ensure that-

(a) records of all plans, drawings and sections required to be made pursuant to regulation 110, are kept in accordance with Regulation 24,

(b) records of all working papers recording observations and calculations which were necessary for the preparation or checking of any plans, drawings and sections prepared pursuant to regulation 110 are kept in accordance with Regulation 24, and

(c) within 3 months of the cessation of mining operations or the permanent abandonment of a mine a complete and accurate set of all plans, drawings and sections and all necessary working papers required to be made pursuant to Regulation 110 are sent to the Authority.

Faulty Plans.

114. 	(1) If an inspector is not satisfied as to-

(a) the competence of the person who prepared any plans, drawings or sections required to be made pursuant to these Regulations , or

(b) the adequacy or accuracy of any plans, drawings or sections required to be made pursuant to these Regulations,

he or she may require that any such plan, drawing or section be prepared by a competent surveyor nominated by the Authority to make a new plan, drawing or section.

(2) The operator shall afford the nominated surveyor referred to in paragraph (1) all such facilities and information as he or she may require in preparing a new plan, drawing or section.

(3) If, as a result of the preparation of a new plan, drawing or section it appears that the opinion of the inspector referred to in paragraph (1) is found to be true, the costs of making the new plan, drawing or section shall be recoverable by the Authority by a simple contract debt in any court of competent jurisdiction and in any legal proceedings the plans, drawings or sections involved shall be received in evidence without further proof unless the contrary is shown.

PART 11

PROVISIONS RELATING TO HOISTING SYSTEMS (INCLUDING SHAFTS)

Appointment and hours of work of hoistman.

115. 	The operator shall ensure that-

(a) no mechanically or gravity operated winding or rope haulage apparatus at a mine is operated for the carriage of persons except by a competent person, who is at least twenty-two years of age and appointed by the operator,

(b) a sufficient number of competent persons are appointed as hoistman for the carriage of persons at the mine,

(c) no person other than an appointed hoistman operates any hoist for the carriage of persons at the mine,

(d) all persons appointed as hoistman for the carriage of persons at the mine hold a current medical certificate indicating that they are medically fit for the position of hoistman,

(e) a hoistman shall not operate a hoist exclusively to raise or lower persons for more than 4 continuous hours,

(f) any second period of 4 continuous hours hoisting of persons cannot be commenced without a break of at least 1 hour, and

(g) the total period of time a hoistman may operate a hoist manually for the hoisting of personnel shall not exceed 8 hours in any 24 hour period.

Hoisting rules.

116. 	(1) Where a mechanical hoisting system is used at a mine, the operator shall prepare or cause to be prepared specific rules, hereinafter referred to as the “hoisting rules”,

(2) A hoisting system at a mine shall include -

(a) the hoist mechanism, both electrical and mechanical,

(b) the buildings in which all electrical and mechanical equipment in relation to subparagraph (a) is located,

(c) the shaft headframe, associated sheave wheels and all materials and personnel related infrastructure,

(d) the shaft, including the infrastructure for the guidance of shaft conveyances,

(e) all services within the shaft, including  pipework, electrical and communications cables and ladderways, and

(f) all infrastructure at shaft stations which is directly related to the safe operation of the shaft, such as barriers, doorways and gates.

(3) The hoisting rules referred to in paragraph (1) shall at a minimum contain provisions in relation to the particulars specified in Schedule 7 and shall be brought to the attention of all persons affected thereby.

Hoist controls, instrumentation and position indicators.

117. 	The operator shall ensure that the hoisting system is fitted with appropriate movement control mechanisms and that all hoist system instrumentation is located in the Hoist Control Centre at the surface of the mine or other approved secure location, and includes -

(a) instrumentation to indicate the approximate position of the shaft conveyance within the shaft whilst the conveyance is travelling at its designed normal operating speed,

(b) instrumentation to indicate to an acceptable level of accuracy, the position of the shaft conveyance when in alignment with a shaft station,

(c) instrumentation to indicate the travelling speed of the shaft conveyance,

(d) instrumentation to indicate the approximate load being transported in the shaft conveyance, and

(e) instrumentation to indicate compliance with designed operating parameters, including current draw, drum rotation speed, bearing temperatures and motor vibration.

Braking systems.

118.	The operator shall ensure that-

(a) the braking capabilities of the hoisting system for the carriage of persons is adequate and in accordance with the standards detailed in the Hoisting Rules,

(b) the hoist control system is designed and maintained to prevent the travelling speed exceeding the rate described in the hoisting rules,

(c) the brakes fitted to a hoisting system comprise more than one set of brakes and each set of brakes is designed such that each set is operated by a separate mechanism,

(d) each braking system shall be capable of stopping safely and holding stationary the maximum design load at the maximum depth of hoisting with a factor of safety of 2,

(e) the braking systems can be operated either automatically or manually, in accordance with the hoisting method in use,

(f) the brakes are applied automatically in the event of a hoisting system electrical, mechanical or other fault or failure, and

(g) the failure of any component on the braking system shall not prevent the hoist system being brought safely to rest.

PART 12

SPECIAL PROVISIONS RELATING TO GASEOUS MINES

Protection from explosion risks.

119.	The operator shall ensure that necessary measures are taken to prevent the formation, accumulation and ignition of explosive atmospheres.

Gassy mines.

120.	 The operator , where firedamp, that is to say any flammable gas or a mixture of gases, naturally occurring at the mine, is likely to be released in such concentrations and quantities that the risk of formation of an explosive atmosphere cannot be excluded, shall ensure that-

(a) the main ventilation is provided by one or more mechanical fans, work proceeds taking account of the firedamp emission and the steps to be taken to eliminate as far as possible the risks arising from firedamp,

(b) auxiliary ventilation is limited to development and salvage work and to places with a direct connection to the main ventilation current, with production workings ventilated by auxiliary systems only if appropriate additional measures are taken to ensure the health and safety of workers,

(c) ventilation measurements required by the ventilation rules are supplemented by regular firedamp determinations,

(d) where specified as necessary in the safety statement, firedamp levels are continuously monitored in return airways from production areas using mechanised extraction or under-winning and at the face of mechanised blind end developments and any other workplaces identified in the safety statement,

(e) automatic alarms and isolation devices are provided to isolate power supplied from electrical installations and to cut off fuel supplies to internal combustion engines,

(f) smoking, carrying tobacco for smoking and other objects which may be used to produce a flame are prohibited, and

(g) flame cutting, welding and other similar operations are carried out only in exceptional circumstances and subject to specific measures to ensure the safety and health of persons employed at the mine.

Mines containing flammable dusts.

121.	The operator of a mine which is susceptible to flammable dusts liable to propagate an explosion shall ensure that -

(a) smoking, carrying tobacco for smoking and any other objects which may be used to produce a flame are prohibited,

(b) flame cutting, welding and other similar operations are permitted only in exceptional circumstances and subject to specific measures to ensure the safety and health of persons employed at the mine,

(c) adequate steps are taken to reduce flammable dust deposits and to remove, neutralise or bind such dust, and

(d) the propagation of flammable dust or firedamp explosions which are liable to trigger further flammable dust explosions are prevented, or where this is not reasonably practicable, limited by installing a system of explosion barriers at all places and in such locations as are identified in the safety statement by a person competent to do so.

Electrical equipment at gassy mines or mines containing flammable dust.

122.	The operator shall ensure that at any part of a mine below ground susceptible to flammable dust liable to propagate an explosion or where it cannot be excluded that flammable gas or a mixture of gases can occur naturally in such concentrations and quantities that there is a risk of formation of an explosive atmosphere, that in that part of the mine-

(a) no electrical equipment shall be used if there is in a risk of incendive sparking or other source of ignition during normal working, and

(b) all rubbing contacts in any motor are arranged or enclosed so as to prevent incendive sparking or other source of ignition.

Fires, spontaneous combustion and heatings.

123.	The operator shall ensure that-

(a) provision is made for the prevention and, where appropriate, the early detection of spontaneous combustion,

(b) the quantity of flammable materials that may be taken into underground workings is no more than is strictly necessary,

(c) where it is necessary to use hydraulic fluids for the transmission of energy, fluids which are difficult to ignite shall, as far as possible, be used in order to avoid the risk of fire and its spread and such hydraulic fluids shall satisfy specifications and test conditions relating to fire resistance and hygiene criteria,

(d) where hydraulic fluids are used that do not satisfy the specifications, conditions and criteria referred to in paragraph (c), additional precautions shall be taken to avoid the increased risk of fire and its spread, and

(e) where spontaneous combustion has been detected, that procedures are in place to minimise the risks to persons employed underground.

Gas outbursts, rock bursts and water inrushes.

124.	The operator shall ensure that-

(a) in zones susceptible to gas outbursts, with or without the projection of minerals or rocks, rock bursts or water inrushes, measures are specified in the safety statement and taken so as to ensure, as far as possible, a safe system of work and the protection of employees, and

(b) the measures referred to in paragraph (a) include measures to identify risk zones, protect persons employed in workings approaching or traversing these zones and control the risks concerned to those persons.

Protection from harmful atmospheres.

125.	The operator shall ensure that-

(a) Where harmful substances accumulate or may accumulate in the atmosphere, appropriate measures shall be taken to ensure -

(i) their suppression at source, or

(ii) their extraction at source or their removal, or

(iii) the dilution of accumulations of such substances in such a way that employees are not at risk,

(b) the measures referred to in paragraph (a) shall be capable of dispersing these harmful substances in such a way that employees are not at risk,

(c) appropriate and sufficient breathing and resuscitation equipment is available in areas where there is a particular risk that employees may be exposed to atmospheres which are harmful to health,

(d) in any place of work referred to in paragraph (c), a sufficient number of employees trained to use equipment of the kind referred to therein shall be present and such equipment shall be suitably stored and maintained.

(e) where toxic gases are, or may be, present in the atmosphere, the safety statement specifies the protective equipment to be provided and the preventive measures to be taken.

Safety equipment.

126.	The operator shall ensure that adequate safety equipment is maintained, ready for use and in good working order at all times and such maintenance is undertaken with due regard to ongoing activities.

PART 13

Air Receivers

Definition of “air receiver” .

127.	In this Part “air receiver” means any of the following:

(a)	a vessel for containing compressed air and connected with air compressing plant, other than -

(i)	a pipe,

(ii)	a coil, or

(iii)	an accessory, fitting or other part of a compressed air plant,

(b)	a fixed vessel for containing compressed air or compressed exhaust gases and used for the purpose of starting an internal combustion engine,

(c)	a vessel forming part of the equipment of a vehicle at a mine for containing compressed air and used to operate the braking system of the vehicle,

(d)	a vessel (not being part of a spraying pistol) used for the purpose of spraying, by means of compressed air, paint, varnish, lacquer or similar material,

(e)	a vessel in which oil is stored and from which it is forced out by compressed air.

Safety precautions.

128.	(1)	Subject to paragraph (2), the operator shall ensure that every air receiver at a mine -

(a)	has the safe working pressure marked on it so as to be plainly visible,

(b)	in the case of an air receiver connected with the air compressing plant, is either constructed so as to withstand with safety the maximum pressure that can be obtained in the compressor, or is fitted with a reducing valve or other suitable appliance to prevent the safe working pressure of the air receiver being exceeded,

(c)	is fitted with a suitable safety valve adjusted so as to permit the air to escape as soon as the safe working pressure is exceeded,

(d)	is fitted with an accurate pressure gauge indicating the pressure in the air receiver,

(e)	is fitted with a suitable appliance for draining the air receiver,

(f)	is fitted with a blow-off cock through which any fluid that may have accumulated in the air receiver may be blown off,

(g)	is provided with a suitable manhole, handhole, or other means that will allow the interior of the air receiver  to be thoroughly cleaned, and

(h)	in a case where more than one air receiver is in use at the mine, bears a distinguishing mark that is easily visible.

(2)	The requirement of paragraph (1)(e) shall not apply to an air receiver referred to in Regulation 127 (d) or (e) and the requirement of paragraph (1)(g) shall not apply to an air receiver referred to in Regulation 127 (c).

(3)	For the purpose of paragraph (1) relating to safety valves and pressure gauges and subject to paragraph (4), any set of 2 or more air receivers supplied with air through a single pipe may be treated as one air receiver.

(4)	In a case where a reducing valve or other suitable appliance to prevent the safe working pressure being exceeded is required to be fitted to a set of air receivers supplied with air through a single pipe, paragraph (3) shall not apply unless the valve or appliance is fitted on the single pipe.

Maintenance and examination.

129.	(1)	The operator shall take all practicable steps to ensure that every air receiver at a mine and its fittings are of sound construction and properly maintained and that the blow-off cock fitted thereto is opened, while the plant is running, at least once in every working day.

(2)	The operator shall ensure that every air receiver at a mine is thoroughly cleaned and examined by a competent person at least once in every period of 2 years, but in the case of an air receiver so constructed that the internal surface cannot be thoroughly examined -

(a)	the person making any such examination may specify in writing a period exceeding 2 years but not exceeding 4 years within which the next examination is to be made, and

(b)	a suitable hydraulic test of the air receiver is carried out in lieu of the internal examination.

(3)	A person carrying out an examination and test under paragraph (2) shall -

(a)	promptly prepare a report containing the particulars as set out in Schedule 8, and

(b)	within 24 hours of completing the examination, provide the report, or a copy thereof, to the person on whose behalf the inspection was carried out.

(4)	Where a report under this Regulation specifies that the safe working pressure of the air receiver to which it relates is to be reduced, or that such air receiver cannot continue to be safely used unless specified repairs are carried out, the operator shall ensure that the air receiver is not used until it is rendered safe, and within 7 days of receiving the report, cause a copy of the report to be sent to the Authority.

(5)	If an inspector is not satisfied as to -

(a)	the competence of the person who carried out an examination under this Regulation, or

(b)	the thoroughness of the examination carried out,

he or she may require the air receiver to be re-examined by a competent person nominated by the Authority, and the operator shall make the necessary facilities available for such re-examination.

(6)	If, as a result of any re-examination under paragraph (5) it appears that the report of the examination under paragraph (2) was inadequate or inaccurate in any respect, the cost of the re-examination shall be recoverable by the Authority from the operator as a simple contract debt in any court of competent jurisdiction and in any legal proceedings the report of the re-examination purporting to be signed by the person making it shall be received in evidence of the facts stated therein without further proof unless the contrary is shown.

PART 14

Safety Provisions for Ancillary Activities and Installations

Definition of “place of work” (Part 14).

130.	In this Part “place of work” means -

(a)	premises at the mine housing workstations, and

(b)	other premises at the mine to which persons at work have access for the purpose of the immediate and ancillary activities and installations of the mine, including premises providing accommodation, rest and sanitary facilities.

Stability and solidity.

131.	The operator shall ensure that a place of work, whether temporary or permanent, has a structure and solidity appropriate to its use, and -

(a)	has been designed and constructed, and

(b)	is operated, supervised and maintained,

so as to withstand the environmental forces anticipated and to be safe and without risk to health.

Floors, walls and ceilings of rooms.

132.	(1)	The operator shall, in respect of a place of work, ensure that -

(a)	floors -

(i)	have no dangerous bumps, holes or slopes, and

(ii)	are fixed, stable and not slippery,

(b)	workstations are adequately insulated, having regard to the type of work activity involved and the physical activity of the persons at work, and

(c)	surfaces of floors, walls and ceilings are such that they -

(i)	can be cleaned, and are cleaned, and

(ii)	where appropriate, refurbished

to an appropriate standard of hygiene.

(2)	The operator shall ensure that transparent or translucent walls, and in particular, glass partitions, in a place of work or in the vicinity of outdoor workstations and traffic routes, are -

(a)	clearly indicated, and

(b)	made of safety material, or are shielded from such places or routes,

in order to prevent persons from coming into contact with such walls or partitions, or being injured in the event of such walls or partitions shattering.

Room dimensions, air space in rooms and freedom of movement at workstations.

133.	The operator shall, in respect of a place of work, ensure that -

(a)	rooms have sufficient surface area, height and air space to allow persons at work to perform their work without risk to their safety, health or welfare, and

(b)	the dimensions of the free space at the workstation allow persons at work sufficient freedom of movement and enable them to perform their work safely.

Windows and skylights.

134.	The operator shall, in respect of a place of work, ensure that -

(a)	windows, skylights and ventilation devices -

(i)	that are meant to be opened, adjusted or secured are designed so that these activities can be carried out in a safe manner, and

(ii)	are not positioned so as to constitute a hazard to persons at work when open, and

(b)	windows and skylights can be cleaned without risk.

Doors and gates.

135.	The operator shall, in respect of a place of work, ensure that -

(a)	the position, number and dimensions of doors and gates, and the materials used in their construction, are determined by the nature and use of the rooms or areas concerned,

(b)	transparent doors are appropriately marked at a conspicuous level,

(c)	swing doors and gates are transparent or have see-through panels,

(d)	if transparent or translucent surfaces in doors and gates are not made of safety material and there is a danger that persons at work may be injured in the event of a door or gate shattering, the surfaces are protected against breakage,

(e)	sliding doors are fitted with a safety device to prevent them from being derailed or falling over,

(f)	doors and gates opening upwards are fitted with a mechanism to secure them against falling back,

(g)	doors forming part of escape routes are -

(i)	appropriately marked,

(ii)	possible to open from the inside at any time without special assistance, and

(iii)	possible to open when the place of work is occupied,

(h)	doors for pedestrians are provided in the immediate vicinity of any gates intended essentially for vehicle traffic, unless it is safe for pedestrians to pass through and such doors are clearly marked and left permanently unobstructed,

(i)	mechanical doors and gates function in such a way that there is no risk of accident to persons at work, are fitted with easily identifiable and accessible emergency shutdown devices and, where they open automatically in the event of a power failure, it is also possible to open them manually, and

(j)	where chains or similar devices are used to prevent access to any place, these are clearly visible and appropriately identified by signs denoting any prohibition or warning.

Ventilation in rooms.

136.	The operator shall, in respect of a place of work, ensure that -

(a)	steps are taken to ensure that there is sufficient fresh air in enclosed rooms, having regard to the working methods used and the physical demands placed on the persons at work,

(b)	where a forced ventilation system is used, it is maintained in good working order,

(c)	any breakdown in a forced ventilation system is indicated by a control system, where this is necessary for the health of persons at work,

(d)	where air-conditioning or mechanical ventilation installations are used, they operate in such a way that persons at work are not exposed to draughts that cause discomfort or ill health, and

(e)	any deposit or dirt likely to create danger to the health of persons at work by entering into the atmosphere is removed without delay.

Temperature in rooms.

137.	The operator shall, in respect of a place of work, ensure that -

(a)	during working hours, the temperature in rooms containing workstations is suitable for the persons at work, having regard to the working methods being used and the physical demands placed on them,

(b)	the temperature in rest areas, rooms for duty staff, sanitary facilities, canteens and first aid rooms is appropriate to the particular purpose of such areas, and

(c)	in relation to windows, skylights and glass partitions, excessive effects of sunlight are avoided, having regard to the nature of the work and the characteristics of the place of work.

PART 15

Health

Health surveillance.

138.	Where an employer at a mine makes health surveillance available to persons at work in accordance with section 22 of the Act, he or she shall ensure that such health surveillance is made available before those persons are assigned to particular work activities in the mine.

Medical Examinations

139. 	(1) Without prejudice to section 23 of the Act, the operator shall cause arrangements to be made for the medical examination and certification of fitness for work by a registered medical practitioner (hereinafter referred to as a “doctor”) of every person to be employed at the mine or required by Regulation 103(d) to have a further medical examination before those persons are assigned to particular work activities in the mine.

(2) Thereafter, as regards any person employed in a mine, the operator shall cause arrangements to be made for the medical examination and certification of fitness for work of that person by a doctor during each twelve months period of service.

(3) A certificate of fitness for work issued for the purpose of this Regulation shall contain the information specified in Form M7 as set out in Schedule 9 and the certification contained in the certificate shall be in terms at least as explicit as the terms of certification so specified.

(4) A certificate mentioned in paragraph (3) may impose conditions or limitations in relation to the employment of persons in any particular capacity or in particular work and may require the person to whom it relates to be further medically examined after a period specified in the certificate.

(5) Every medical examination carried out for the purpose of this Regulation may consist of any or all of the following -

(a) a general clinical examination,

(b) a blood pressure determination,

(c) a haemoglobin estimation,

(d) an X-ray examination of the lungs,

(e) respiratory function tests,

(f) a blood lead level determination,

or any other medical examination which may be reasonably required by the doctor.

(6) Every person so examined shall be examined at the expense of the operator.

(7) A record of every certificate issued under this Regulation shall be kept in accordance with Regulation 24.

(8) The operator of a mine shall, before the employment of a person at a mine, cause notice to be given to—

(a) the doctor by whom that person is to be examined, of the name, address and age of the person, and

(b) the person requiring him to attend that doctor for examination on a day and time specified in the notice.

(9) Where any person employed at a mine is required by a certificate issued for the purpose of these Regulations to be further medically examined, the mine manager shall, not later than four days before the end of the period specified in the certificate, cause notice to be given to—

(a) the doctor by whom the person is to be examined, of the name, address and age of the person together with particulars of the certificate, and

(b) the person requiring him to attend that doctor for further examination on a day and time specified in the notice,

within or not later than fourteen days after the end of the period specified in the certificate.

(10) A person shall comply with the requirements of a notice given to him or her under paragraphs (8) and (9), and any person who fails so to comply shall not be employed at the mine.

(11) The operator shall ensure that a person shall not be employed at a mine unless the requirements of these Regulations as to medical examinations have been complied with and a current certificate of fitness has been issued under these Regulations, and—

(a) in case such a certificate is issued in relation to the employment of the person in a particular capacity or particular work, he or she shall not be so employed in any other capacity or work, and

(b) in case such a certificate is a certificate issued for a limited period specified in the certificate, the person shall not be so employed after the expiration of the period so specified, unless or until a further certificate of fitness is issued in relation to that person.

Health hazards.

140.	(1)	The operator, where persons are liable to be exposed to any chemical, physical or biological hazard to such an extent as is liable to be dangerous to health, shall ensure that appropriate preventive measures are taken at the mine against that exposure.

(2)	The preventive measures referred to in paragraph (1) shall include -

(a)	wherever possible, the replacement of a hazardous substance by a harmless or less hazardous substance,

(b)	technical measures applied to the plant, machinery, equipment or process, or

(c)	where it is not possible to comply with subparagraph (a) or (b), other effective measures, including the use of personal protective equipment and protective clothing.

Atmospheric influences.

141.	The operator shall ensure that persons working outdoors at the mine are protected against atmospheric conditions that could affect their safety and health.

Disposal of waste.

142.	The operator shall ensure that waste from the mine is not -

(a)	destroyed, or

(b)	otherwise disposed of

in a manner liable to be injurious to the safety and health of persons.

Stationary internal combustion engines and exhaust gases.

143.	The operator shall ensure that -

(a)	no stationary internal combustion engine is used at the mine in any enclosed or confined place, unless specific provision is made for conducting the exhaust gases from the engine into the open air or ventilation airway, or

(b)	any such enclosed or confined place is adequately ventilated so as to prevent danger to health from the exhaust gases.

PART 16

Welfare

Shelters and accommodation for clothing and taking meals.

144.	(1)	The operator shall ensure that, subject to paragraphs (2) and (3), there is provided at or in the immediate vicinity of the mine for the use of persons at work and conveniently accessible to them -

(a)	adequate and suitable enclosed accommodation for taking shelter during interruptions of work owing to bad weather and for depositing clothing not worn during working hours, being accommodation containing, where practicable, adequate and suitable means of enabling such persons to warm themselves and to dry wet clothing,

(b)	adequate and suitable accommodation for the deposit of protective clothing used for work and kept, when not in use, at or in the immediate vicinity of the mine with such arrangements as are practicable for drying such clothing if it becomes wet,

(c)	adequate and suitable accommodation affording protection from the weather and including sufficient tables with impermeable surfaces and seats with backs for taking meals,

(d)	facilities for boiling water and, where there are more than 5 persons at work at a mine and heated food is not otherwise available at the mine, adequate facilities for heating food, and

(e)	an adequate supply of potable drinking water and possibly another suitable non-alcoholic beverage at a convenient point or convenient points.

(2)	For the purposes of paragraph (1), in determining whether accommodation is conveniently accessible, account shall be taken of any transport provided for the persons at work.

(3)	For the purposes of paragraph (1)(c), in determining whether accommodation of any kind provided in pursuance of that subparagraph at any time and place is adequate, account shall be taken of the number of persons at work who appear likely to use such accommodation at that time and place.

(4)	The operator shall ensure that all accommodation provided in accordance with this Regulation is -

(a)	properly ventilated, adequately lighted, kept in a clean, hygienic and orderly condition, and

(b)	not used for the deposit or storage of materials or plant.

Changing rooms and lockers.

145.	(1)	An operator shall provide or cause to be provided -

(a)	appropriate changing rooms for persons at work if they have to wear special work clothes and if, for reasons of health or propriety, they cannot be expected to change in another area, which are -

(i)	easily accessible,

(ii)	of sufficient capacity, and

(iii)	provided with seating,

(b)	separate changing rooms or separate use of changing rooms for men and women, and

(c)	adequate provision for drying wet or damp work clothes.

(2)	If circumstances so require where work clothes are likely to be contaminated by dangerous substances, atmospheric conditions or the conditions of the place of work, the operator shall provide, or cause to be provided, facilities in changing rooms to enable working clothes to be kept in a place separate from personal clothing and effects.

(3)	If changing rooms are not required as referred to in paragraph (1), the operator shall ensure that every person at work is provided with a place to store his or her own clothes and personal effects.

Washing facilities.

146.	(1)	The operator shall ensure that adequate and suitable facilities for washing appropriate to the numbers of persons at work and the duration of the work are provided at the mine, including -

(a)	adequate troughs or washbasins having in every case a smooth impervious internal surface,

(b)	adequate and suitable means of cleaning and drying, being either soap and towels or other means, as the case may require, and

(c)	a sufficient supply of hot and cold or warm running water.

(2)	The operator shall ensure that -

(a)	washing facilities provided are conveniently accessible from the accommodation for taking meals and are adequately lighted, properly ventilated and are kept in a clean and orderly condition,

(b)	provision is made for separate washbasins, or separate use of washbasins for men and women when so required for reasons of propriety,

(c)	suitable showers in sufficient numbers are provided for persons at work, if required by the nature of the work or for health reasons,

(d)	provision is made for separate shower rooms or separate use of shower rooms for men and women,

(e)	the shower rooms are sufficiently large to permit each person to wash without hindrance in conditions of an appropriate standard of hygiene and such showers are equipped with hot and cold running water, and

(f)	where the rooms containing showers or washbasins are separate from changing rooms, there is easy access between the two.

Sanitary conveniences.

147.	(1)	The operator shall ensure that adequate and suitable sanitary conveniences appropriate to the number of persons at work at the mine are provided.

(2)	The operator shall ensure that -

(a)	every sanitary convenience, other than a convenience suitable only as a urinal, has a proper door fastening and is partitioned off to secure privacy,

(b)	every sanitary convenience required to be provided is sufficiently ventilated and does not communicate with any workroom or mess room except through the open air or through an intervening ventilated space,

(c)	every sanitary convenience is under cover,

(d)	the sanitary conveniences are so arranged as to be conveniently accessible to persons at work at all times while they are at the mine and are, where practicable, convenient to the washing facilities,

(e)	provision is made for separate sanitary conveniences or separate use of sanitary conveniences for men and women, and

(f)	every sanitary convenience is maintained in a clean and hygienic condition.

Safe access to places where facilities are provided.

148.	The operator shall ensure that -

(a)	safe means of access and egress is provided and maintained to and from every place at which any facilities provided in accordance with this Part are situated, and

(b)	every such place is made and kept safe for persons using such facilities.

Pregnant women and nursing mothers.

149.	The operator shall ensure that pregnant women and nursing mothers at work at the mine are provided with appropriate facilities as set out in other relevant legislation.

Persons with disabilities.

150.	The operator shall, where necessary, ensure that a mine is organised to take account of persons at work with disabilities, in particular as regards doors, passageways, staircases, showers, washbasins, lavatories and workstations used or occupied directly by those persons.

Rest rooms.

151.	The operator shall ensure that -

(a)	where necessary, and in particular, where the number of persons at work requires it, they are provided with an easily accessible rest room,

(b)	rest rooms are large enough and equipped with tables, and with seats with backs, adequate for the number of persons at work, and

(c)	if working hours are regularly and frequently interrupted and there is no specific rest room, other rooms are provided in which persons at work can stay during such interruptions, where this is required for their safety or health.

SCHEDULE 1

Regulation 8

Notifications to the Authority

Notification of Appointment or Change of Operator/Common Operator, Commencement or Permanent Cessation of Mining Operations.

FORM M1

I hereby give notice of (delete as appropriate);

-Appointment/ change of operator

-Appointment/ change of common operator

- Commencement of mining operations

- Permanent cessation of quarrying operations.

Name of Person or Company under which the business is carried on:

_________________________________________________________________________

Name of Operator/Common Operator:

__________________________________________________________________________

Signature of or behalf of Operator:

______________________________________________

Date:

_________________________________

Address:

_________________________________________________________________________

__________________________________________________________________________

Telephone Number: __________________________Fax ___________________________

Number:_________________________________

Name of Mine: __________________________

Place where Mine is situated: __________________________

State townland:__________________________

Ordnance survey grid references: __________________________

Date when operations are to commence/cease: __________________________

or

Change of operator is to take affect: __________________________

Notifications of Dangerous Occurrences

Form M2

Form of Notice of Dangerous Occurrence

1. Name of Mine ………………………………………………………………………………

2. Address of Mine ……………………………………………………………………………..

…………………………………………………………………………………………………..

…………………………………………………………………………………………………..

3. Name and Postal Address of Mine Manager ………………………………………………...

…………………………………………………………………………………………………..

…………………………………………………………………………………………………..

4. Date and hour of dangerous occurrence ……………………………………………………..

5. Place of dangerous occurrence …………………………………………………………........

…………………………………………………………………………………………………..

6. Cause and description of dangerous occurrence:

7. If machinery was involved, state:

(i) Name and type of machine ……………………………………………………….

(ii) Part of machine involved ………………………………………………………….

(iii) Whether in motion by mechanical power at the time ……………………………

8. If explosives were involved, state:

(i) Name of explosive …………………………………………………………………

(ii) How fired ………………………………………………………………………….

(Signed) ………………………………………….. Mine Manager.

Date ……………………. 20….

SCHEDULE 2

Regulations 15, 31 and 103

Mines Skills Training Scheme

Part A – Relevant Tasks

The requirement for the mines skills training scheme requires training to be given under the scheme in any of the following tasks:

(a)	slinging and signalling;

(b)	telescopic handler operation;

(c)	tractor and dozer operation;

(d)	mobile crane operation;

(e)	crawler crane operation;

(f)	articulated dumper operation;

(g)	site dumper operation;

(h)	180° excavator operation;

(i)	mini-digger operation – where the person has not been trained in the task referred to at subparagraph (h);

(j)	360° excavator operation;

(k)	rigid dump truck operation;

(l)	front end loader operation;

(m)	LHD (load haul dump) scooptram operation;

(n)	explosives storekeeping;

(o)	shotfiring;

(p)	explosives supervision;

(q)	mine rescue; or

(r) 	such other mining-related tasks as may be prescribed by the Minister.

Where it is necessary to gain experience prior to undertaking a programme related to the tasks listed above it is permissible for a person to undertake those tasks, if the person concerned is at all times under the close personal supervision of a person who is a training officer, an instructor or a person in possession of a current certificate of authorisation relevant to the task concerned.

Part B – General Requirements

(1) The operator of every mine shall appoint a safety training officer to superintend the implementation of a mines skills training scheme at that mine.

(2) The duties of a safety training officer shall include the—

(a) the superintending of training, retraining or supervision during such required to be given or

provided for the training scheme,

(b) keeping of a training record of the training or retraining given in pursuance of the training scheme for the mine and the furnishing, at such times as the operator of the mine may request, of reports to him or her on the progress of each person undergoing such training or retraining,

(c) making of recommendations to the mine manager as to the training of any person employed at the mine for employment on work for which the person has no previous training,

(d) making of recommendations to the mine manager of the mine as to the retraining of any person employed at the mine on any operation,

(e) certifying to the mine manager that a person has completed his training or retraining, as the case may be, and, in the case of a person undergoing training for employment on work for which he or she had no previous training, that he or she is competent to do that work without supervision.

(3) A safety training officer may be appointed on a part-time basis if there are less than 300 persons normally employed at the mine and, in every other case, he or she shall be appointed on a full time basis.

(4) The mine manager shall appoint one or more persons to act as instructors at the mine

(5) The mine manager shall ensure that any person appointed as an instructor—

(a) is qualified to give instruction and supervision in the performance of the work in which instruction and supervision are being given,

(b) is required to devote his or her whole time to giving instruction and supervision while a training scheme is in progress, and

(c) does not perform or assist in the performance of the work in which he or she is giving instruction and supervision otherwise than for the purpose of demonstration.

(6) The mine manager of a mine shall maintain at the mine the training scheme for the mine or any proposed variation of an existing training scheme setting out particulars of the manner in which the requirements in relation to training or retraining are to be complied with.

(7) Every training scheme shall include provisions relating to—

(a) the training of persons for work either at the surface of the mine or in the mine below ground or to both;

(b) a description of each task or operation for which, in the opinion of the mine manager, training or retraining is required;

(c) the minimum period of time allowed for training or retraining for a particular operation;

(d) the appointment of a competent person to act as a safety training officer;

(e) the appointment of competent persons to act as supervisors or instructors.

(8) The mine manager shall ensure that a copy of the training scheme is available to each person who is affected by the scheme.

(9) The mine manager shall take all practicable steps to ensure that a person to be employed in the mine in work below ground for which training is required under these Regulations shall not be so employed unless he has received the training described in this Scheme and there is at the mine a certificate issued by the mine manager of, or the safety training officer for, the mine, stating that the person has received such training and is competent.

(10) The training referred to above is training which—

(a) is given to a person during the working hours during which he or she may be lawfully employed at a mine,

(b) comprises adequate instruction in safe methods of working below ground in a mine, and

(c) is given by and under the close personal supervision of an instructor or supervisor.

(11) When a person has completed the training described he or she shall be given a copy of the certificate referred to which shall be in the form specified in Form M3 as set out in Part E.

(12) The requirements of the mines safety training scheme are in addition to training required pursuant to Section 10 of the Act.

(13) The operator shall take all practicable steps to ensure that a person to be employed in work at the surface of the mine for which training is required under these Regulations (other than work for which a recognised apprenticeship is required) shall not be so employed unless he or she has received a certificate issued by the mine manager stating that he or she has received such training and is competent.

(14) The training referred to above is training which—

(a) is given to a person during the working hours during which the person may be lawfully employed at a mine,

(b) comprises adequate instruction in safe methods of working, and

(c) is given by and under the close personal supervision of an instructor or supervising workman.

(15) When a person has completed the required training he or she shall be given a copy of the certificate referred to which shall be in the form specified in Form M3 as set out in Part E.

(16) The mine manager of a mine shall ensure that adequate arrangements are made for conducting refresher courses at the mine in order that the expertise of the persons employed there may be brought up to date as and when required.

(17) Every person employed at a mine shall comply with such directions concerning training or retraining as may be given to him or her by or on behalf of the operator and no person shall be employed in an operation for which he or she requires training or retraining unless he or she complies with those directions.

(18) Subject to Regulation 24 the records and reports relating to each person employed at a mine which are required to be made under these Regulations, or a training scheme for the mine, shall be kept together in one place at the mine or at such other place as may be approved of by an inspector in writing.

(19) Every person employed at a mine shall be entitled at all reasonable times to inspect his or her personal training record.

Part C - Scheme for Instruction and Practices in Rescue Work

Instruction

(1) The course of initial instruction shall include instruction as to:

(a) the general methods of dealing with underground fires and the recovery of mines after fires and explosions,

(b) the construction, use, repair, maintenance and testing of the type or types of breathing apparatus provided and of smoke helmets or other apparatus serving the same purpose,

(c) the use of methods and apparatus for reviving persons,

(d) the properties and detection of the noxious and flammable gases which may be found in mines,

(e) the taking of gas samples in irrespirable atmospheres,

(f) the reading of mine plans, and

(g) the conduct of rescue work detailed in these Regulations and the code of signals contained in Part D.

Practices

(2) Not less than 12 practices shall be provided for each person using breathing apparatus together with not less than two practices using smoke helmets or other apparatus serving the same purpose. Every practice shall take place under conditions so devised as to simulate those likely to be encountered in underground operations requiring the use of such apparatus.

(3) The practices shall be carried out as far as possible by each rescue team as such, i.e. by all members of the team, at one and the same time.

(4) The practices with breathing apparatus shall take place initially in ordinary air and shall thereafter progress gradually until practices can be carried out in an irrespirable atmosphere.

(5) Subject to paragraph (6), the practices with breathing apparatus shall comprise the following operations, namely:

(a) the repeated raising and lowering of a weight of 25.4 kilogrammes (56 lbs. to and from a height of 1.83 meters (6 feet) by means of a rope and pulley;

(b) walking continuously at a fair pace for half-an-hour,

(c) building and removing temporary stoppings of stone, brick, sandbags, brattice cloth or other materials, and carrying the materials required for such operations over a distance of at least 9.14 meters (30 feet),

(d) removing debris in confined spaces as representing the clearing of a fall of roof,

(e) setting timber or other roof supports,

(f) carrying, pushing or pulling on a stretcher a live person or dummy body weighing at least 68.2 kilogrammes (150 lbs), along the length of a gallery, and through an opening 0.6 meters (2 feet) high by 0.91 meters ((3 feet) wide and 3.64 meters (12 feet) long, and

(g) the rapid establishment of communication.

(6) An operation which an inspector considers appropriate may be used in practices with breathing apparatus in lieu of an operation mentioned in paragraph (5).

Instruction after initial training

(7) Revision of all subjects included in the course of instruction and practice specified in the foregoing paragraphs of this Schedule.

Practices after initial training

(8) The practices shall be with breathing apparatus and shall take place at least once in each quarter and at least six times annually, and at least two of the practices shall take place in mines, and the remainder in an irrespirable atmosphere.

(9) Where possible mine practices shall include work in low and constricted roadways.

(10) All practices required by this part of this Schedule shall last at least two hours except on occasion when, in the opinion of the instructor, it is desirable in the interests of safety to curtail the practice. At some of the practices the breathing apparatus shall be worn continuously for two hours.

Part D - All Team Members Code of Signals

All team members shall be trained in an established Code of Signalling

Electric Signalling

To be used where a two way telephone communication system is not in use between the fresh air base and the rescue team.

| Signal | Message |
| --- | --- |
| ONE ring | “Distress” or “Help wanted” |
| TWO rings * | “Not understood” or “Repeat the Message” |
| THREE rings | “No” |
| FOUR rings * | “Yes” or “All right” or “All's well” |
| FIVE rings * | To “ring up”. To “ring off” |
| *If no answer is received distress is to be understood. |  |

Audible Signaling between Members of a Rescue Team

| Signal | Message |
| --- | --- |
| ONE hoot | “Distress” or “Help wanted” |
| TWO hoots | Halt |
| THREE hoots | Retire |
| FOUR hoots | Advance |
| FIVE hoots | To call attention |

Certificate of Appointment

Form M3

I HEREBY CERTIFY THAT-

(a) ............................................................ ......................................... ...........................................

who is .............. years of age has received the necessary training for employment as -

(b) ............................................................ .......................................... ...........................................

and, in my opinion is competent to carry out the following duties (c) .........................................

............................................................ ............................................................ ...............................

............................................................ ............................................................ ...............................

Signed ............................................................ ............................................................ ...................

Manager for the ......................................................... . Mine

Date............................................................ ....

Notes:

(a) Insert full name and address

(b) Insert nature of intended employment

(c) Insert precise scope of duties

SCHEDULE 3

INSPECTION REPORT FORMS

Regulations 18, 27 and 28

SAFETY, HEALTH AND WELFARE AT WORK (MINES) REGULATIONS 2010

FORM M4

REPORTS ON PRE-SHIFT INSPECTIONS

By Duputy/ Shift Boss or appointd person

(Regulation 27)

Name and address of Mines:

________________________________________________________________________

________________________________________________________________________

REPORT ON PRE-SHIFT INSPECTION BY DEPUTY/ SHIFT BOSS/ APPOINTED PERSON

Mine: __________________________________________________________________

Working area: ___________________________________________________________

Shift: __________________________________________________________________

Date: __________________________________________________________________

I certify that I have mayself inspected every part of the above-named area/workplace that is required to be ventilated and that the following is a full and accurate report of the condition of the area/ workplace as ascertained by me:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

If gas was found state place and circumstances of each occurence and action taken. If not found record the fact.

Conditions of Ventilation:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

State actual conditions. If any defects or interruptions give particulars, say how caused and action taken.

Condition of Roof and Sides:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

State actual condition of (a) working faces and (b) roads, with location of any unsafe place and action taken.

Other Sources of Danger and Remarks:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Conditions of Dust Suppression Equipment: Give details of any shortage or defects:

(If space is insufficient continue report on back of this form).

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Inspection Commence - a.m/- p.m.

(Strike out whichever does not apply)

Signed (Deputy/ shift boss or appointed person in charge of the working areas):

_____________________________

Inpection – a.m.

Completed – p.m.

Shift – p.m.

Time of commencement of work in – a.m.

(Signature of mine manager or other person appointed under Regulation 12 of the Safety, Health and Welfare at Work (Mines) Regulations 2010 to read these reports on his or her behalf:

_____________________________

Date:

_____________________________

SAFETY, HEALTH AND WELFARE AT WORK (MINES) REGULATIONS 2010

FORM M5

Book for

DEPUTY’S (SHIFT BOSS’S) GENERAL INSPECTION REPORTS

Name and address of Mine:

__________________________________________________________________________

__________________________________________________________________________

GENERAL REPORT ON HIS SHIFT BY DEPUTY/ SHIFT BOSS IN CHARGE OF WORKING AREA

Date:_____________________________

Shift: _____________________________

Mine: _____________________________

Working Area: _____________________________

PART A

Period covered by my shift a.m/p.m to (*Maximum number of workmen in my charge as recorded under)

Name of any substitute appointed under Regulation 18 and period for which he was appointed.

Times at which inspections required were made.

Nature of Inspection and Place or Place Inspected.

Commenced							Completed

a.m. / p.m.							a.m. /p.m.

a.m. / p.m.							a.m. /p.m.

a.m. / p.m.							a.m. /p.m.

a.m. / p.m.							a.m. /p.m.

Delete whichever is not applicable.

PART B

Time

(If space is insufficient continue report on back of this form)

I certify that this report is a full and accurate record of the preformance of all duties during my shift and of everything known to me which has accoured which is material to the proper working of the mine or the safety or health of persons employed in the working area.

Signed:_______________________________

Date:_________________________________

Deputy/Shift Boss in charge of the working area:

_____________________________________

Counter signature of superior official.	Signature of mine manager or other person appointed under Regulation 12 of the Safety, Health and Welfare at Work (Mines) Regulations 2010 to read these reports on his or her behalf:

______________________________________

Date:

SAFETY, HEALTH AND WELFARE AT WORK (MINES) REGULATIONS 2010

FORM M6

PART A

Book for Reports of

REPORTS OF INSPECTIONS OF PARTS OF A MINE WHERE PERSONS REGULARLY PASS

Name and address of mine:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Date of Inspection;

______________________________________________

______________________________________________

______________________________________________

Place or places inspected:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Full and accurate report of condition disclosed by inspection, and action taken or necessary to deal with any defect or source of danger:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Signature of competent person making the inspection:

______________________________________________

______________________________________________

______________________________________________

Signature of mine manager or person appointed under Regulation 12 of the Safety, Health and Welfare at Work (Mines) Regulations 2010t to read these reports on his or her behalf:

______________________________________________

Date:

PART B

Book for

REPORTS OF WEEKLY INSPECTIONS OF AIRWAYS, TRAVELWAYS AND ROADS NOT WITHIN THE WORKING AREA OF DEPUTY / SHIFT BOSS

Name and address of mine:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

REPORT OF INSPECTION OF PARTS OF A MINE, WHERE PERSONS REGULARLY PASS

Date of Inspection:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Places or places inspected:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Full and accurate report of condition deisclosed by inspection, and action take or necessary to deal with any defect or source of danger:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Signature of competent person making the inspection:

______________________________________________

______________________________________________

______________________________________________

______________________________________________

______________________________________________

Signature of mine manager or other person appointed under Regulation 12 of the Safety, Health and Welfare at Work (Mines) Regulations 2010 to read these reports on his or her behalf:

Date:

SCHEDULE 4

Regulation 22

PROCEDURES FOR THE SELECTION OF A MINE SAFETY REPRESENTATIVE

1.	In the absence of a mine safety representative selected by the persons at work at a mine the following procedures shall apply as regards the selection of a mine safety representative -

(a)	If a mine safety representative is elected by the workers at the mine at any time after commencement of activities at the mine this person shall be recognised as such by the operator of the mine and particulars shall be noted in writing by the operator of the mine.

(b)	If a safety representative has previously been selected under section 25 of the Act by the employees or, if the mine is worked by contractors, by any of the contractors at the mine, the views of all persons at work at the mine at the time shall be taken into account when confirming that person as mine safety representative.

(c)	If, at the time the number of persons at work at the mine normally exceeds 10 and there is no mine safety representative, the operator of the mine shall invite all persons working at the mine at that time to elect a mine safety representative from amongst their number. If those working at the mine are unwilling to organise a selection process themselves and request the operator of the mine to do so he or she shall organise the election.

(d)	If a mine safety representative is not selected under subparagraph (c) the operator of the mine shall invite persons working at the mine or their representatives to nominate persons willing to undertake the role. If more than one name is submitted to the operator of the mine he or she shall determine which candidate has the most support from all persons employed at the mine. The person who has the most support shall be deemed selected.

(e)	If no mine safety representative has been selected under subparagraphs (a) to (d) the mine operator shall nominate a provisional mine safety representative. If subsequently a mine safety representative is elected in a process involving more than 50 percent of the persons working at the mine at a particular time then that person shall be deemed to be the mine safety representative.

(f)	The mine operator shall take steps to inform all persons who are at work at the mine at the time of the selection and subsequently of the name of the mine safety representative and shall keep available for inspection by an inspector a record of the name of the mine safety representative and details of the selection process.

2.	For the purposes of Regulation 23, a committee of persons with suitable practical experience of mining operations may be appointed for the mine and the mine safety representative shall be a member of the committee.

3.	Where an injury or dangerous occurrence which is reportable under any of the relevant statutory provisions occurs at a mine, the operator shall permit 2 members of the committee appointed under paragraph 2, which may include the mine safety representative, to inspect together the place where the injury or dangerous occurrence occurred so as to ascertain its cause.

4.	The operator of a mine shall permit sufficient inspections to be carried out by members of the committee appointed under paragraph 2 to enable every part of the mine and any plant and work equipment at the mine to be inspected regularly and at intervals not exceeding 13 weeks by 2 of those committee members together.

5.	The operator of a mine shall make available to members of a committee appointed under paragraph 2 who are carrying out an inspection under paragraph 4 -

- any documents which are kept at the mine in compliance with the relevant statutory provisions, and

- the safety statement referred to in Regulation 13.

6.	The operator of a mine may facilitate members of a committee appointed under paragraph 2 who are carrying out an inspection as specified in paragraph 4 with access to external advice.

SCHEDULE 5

Regulations 29 and 37

Vehicles Requiring Auxiliary Devices and Visual Aids

| Machine Type | Reversing and visual aids required |
| --- | --- |
| Off-road dump trucks (trailer to rear of driver) - payload greater than 7 tonnes | Reversing alarm and flashing beacon with CCTV or convex mirrors or a combination of both to allow vision from the driver’s seat of all points more than 1 metre high and 1 metre from the machine at each side and at the rear of the driver |
| Dumpers (front tip) no cab | Reversing alarm and flashing beacon |
| Dumpers (front tip) with cab | Convex mirrors; reversing alarm and flashing beacon |
| Wheel loaders (loading shovels, scooptrams), including skid steer loaders | Reversing alarm and flashing beacon with CCTV or convex mirrors or a combination of both to allow vision from the driver’s seat of all points more than 1 metre high and 1 metre from the machine at each side and at the rear of the driver |
| Backhoe loaders (JCB type machines) | Convex mirrors; reversing alarm and flashing beacon |
| 3600 excavators | Movement alarm and flashing beacon with CCTV or convex mirrors or a combination of both to allow vision from the driver’s seat (without slewing) at all points more than 1 metre high and 1 metre from the machine |
| Scrapers (bulldozers) | Reversing alarm and flashing beacon with CCTV or convex mirrors or a combination of both to allow vision from the driver’s seat of all points more than 1 metre high and 1 metre from the machine at each side and at the rear of the driver |
| Tracked type tractors (bulldozers) | Reversing alarm and flashing beacon with CCTV or convex mirrors or a combination of both to allow vision from the driver’s seat (without slewing) at all points more than 1 metre high and 1 metre from the machine at each side and at the rear of the driver |
| Graders | CCTV, convex mirrors, reversing alarm and flashing beacon |
| Telescopic handlers | Reversing alarm and flashing beacon with CCTV or convex mirrors or a combination of both to allow vision from the driver’s seat of all points more than 1 metre high and 1 metre from the machine at each side and at the rear of the driver |

SCHEDULE 6

Regulation 59

Geotechnical Assessments

Documents and Particulars to be included in Geotechnical Assessment

Excavation, tip or lagoon.

1.	In this Schedule “excavation, tip or lagoon” includes, where appropriate, a proposed excavation, tip or lagoon.

Site survey.

2.	An accurate plan on a scale not less detailed than 1:2,500 showing -

(a)	the boundaries of the mine upon which the excavation, tip or lagoon is or is to be situated,

(b)	the location of the excavation, tip or lagoon,

(c)	any contiguous land, strata or structure that might be affected by the excavation, tip or lagoon,

(d)	old mine workings, known cave systems, active or former landslips, springs, artesian wells, watercourses, mine workings (whether in use or not) and other natural or man-made features, including tunnel pipes or culverts that might -

(i)	affect the safety of the excavation, tip or lagoon, or

(ii)	be relevant for the purpose of determining whether mining operations can be carried out safely.

This plan shall be contoured, orientated and correlated to the Ordnance Datum Survey National Grid at a vertical interval not greater than 5 metres and marked with squares corresponding to the 100 metre squares shown on Ordnance Survey sheets on the scale of 1:2,500.

Site investigation.

3.	A record of all relevant site investigation information including surveys, tests, boreholes and groundwater measurements made for the purpose of the geotechnical assessment together with the results of any testing including the strength of materials within and beneath the tip or within the excavation. The record shall include any known historical information relevant to the site investigation.

Cross-sections based on site investigation.

4.	Sufficient accurate cross-sections on a scale not less detailed than 1:1,250 of the site of the excavation, tip or lagoon showing the existing excavations, ground surface and all relevant superficial materials and bedrock underlying the site and -

(a)	any variation in the thickness, level or character of the superficial deposits and bedrock materials based on the site investigation; and

(b)	the position of any surface, whether natural or man-made, that may affect the safety of the excavation, tip or lagoon.

Plans based on site investigation.

5.	Plans showing the position of all boreholes, wells and trial pits used in the site investigation and the location and levels of all materials and surfaces that may affect the safety of the excavation, tip or lagoon.

Assumptions made before analysis.

6.	A record of any assumptions relevant to the assessment of ground conditions relating to the safety of the excavation or tip made by the geotechnical specialist, including a record of any relevant information that was not available when undertaking the assessment.

Findings of analysis.

7.	A record of the calculations carried out in order to determine the safety of the excavation or tip, including any variables or parameters used in those calculations and the reasons for using them and the findings of those calculations expressed as the factor of safety or the probability of failure or other recognised basis of assessing stability.

Design coming out of analysis.

8.	An accurate plan on a scale not less detailed than 1:2,500 recording -

(a)	in relation to an excavation, the design of the excavation, including the overall dimensions or proposed dimensions of the excavation, the position and dimensions of any development drifts and representative contours of the excavation at vertical intervals of not more than 1 metre, and

(b)	in relation to a tip or lagoon, the design of the tip or lagoon, including the area of land covered or to be covered, the gradients of that land, the designed contours at vertical intervals of not more than 2 metres, the side slopes and boundaries of the tip or lagoon and the designed position and nature of construction of any wall or other structure retaining or confining the tip, or lagoon.

Requirements during and after mining operations.

9.	A report of the nature and extent of inspection, supervision and safety measures necessary to ensure the safety of the excavation, tip or lagoon and a specification of necessary engineering works and safety measures.  A record of the action to be taken regarding defects shall be specified in the report.

SCHEDULE 7

Regulation 116

HOISTING RULES

Safety requirements

(i) at shaft top,

(ii) at shaft bottom, and

(iii) at shaft stations.

Design of hoisting system

approved by a competent person.

Shaft hoisting mechanisms

(i) braking systems,

(ii) speed control, to include prevention of overwind and underwind,

(iii) instrumentation, and

(iv) shaft conveyance position.

Training, authorisation of persons and record keeping

(i) hoist operator training,

(ii) shaft maintenance crew training,

(iii) hoist maintenance crew training,

(iv) training of personnel to operate push-button hoisting systems, and

(v) record keeping regime for inspections and routine checks.

Operation of systems when carrying materials

(i) ratio of load to be hoisted relative to rope specification,

(ii) travelling speed,

(iii) acceleration and deceleration speeds, and

(iv) prevention of spillage of material during hoisting.

Operation of systems when carrying persons for maintenance purposes

(i) safety of persons whilst carrying out maintenance within the shaft,

(ii) suitability of shaft skip for carrying persons,

(iii) travelling speeds,

(iv) acceleration and deceleration speeds,

(v) communication between persons in the shaft and the hoist operator, and

(vi) frequency of shaft inspection.

Maintenance and testing

(i) procedures for daily inspection and testing of the hoisting system,

(ii) frequency of rope inspection,

(iii) frequency of rope testing,

(iv) policy on rope replacement,

(v) policy on shaft guides and supporting structures,

(vi) skip to be independently supported while maintenance work is underway on skip, and

(vii) record keeping method for all maintenance work carried out.

Emergency Procedures

(i) use of the hoist for emergency purposes,

(ii) assembly arrangements at shaft stations, and

(iii) effects of mine ventilation on use of shaft.

Hoisting of personnel

safety precautions to prevent uncontrolled descent of the cage whilst carrying personnel.

SCHEDULE 8

Regulation 129

Air Receivers

Particulars to be Included in Report of Examination of Air Receiver

1.	Name of operator of mine.

2.	Name and address of mine.

3.	Description, distinguishing mark and type of the air receiver.

4.	Date of construction (if ascertainable) together with a brief history of the air receiver.

5.	Date of last hydraulic test (if any) and pressure applied.

6.	Particulars of -

(a)	inaccessible parts (if any) at the time of examination,

(b)	the examination and test made,

(c)	its condition, including particulars of any defect materially affecting the safe working pressure.

7.	Particulars as to whether the fittings and appliances are properly maintained and in good condition.

8.	Particulars of the safe working pressure calculated from dimensions, thickness and other data as ascertained during the examination, taking account of unusual or exceptionally severe working conditions.

9.	Particulars of -

(a)	repairs (if any) required,

(b)	the period within which the repairs should be carried out, and

(c)	any other requirements that the person making the examination considers necessary.

10.	Where repairs affecting the safe working pressure are required under paragraph 9, particulars of the safe working pressure that shall apply to the air receiver -

(a)	before the expiration of the period specified in paragraph 9(b),

(b)	after the expiration of such period, if the required repairs have not been completed, and

(c)	after the completion of the required repairs.

11.	The date of the examination and the name of the competent person who carried it out.

SCHEDULE 9

Regulation102 and 139

Certificate of Medical Examinations

FORM M7

Reference No.……………

Certificate of Fitness for Employment –

I certify that I have examined the following person having regard in particular to sight, hearing and heart.

(Name in Full) …………………………………………….

Whose address is ……………………………………………………………………………………

……………………………………………………………………………………………………….

……………………………………………………………………………………………………….

Date of Birth …………………………………..

I find that person fit for employment to the extent specified and subject to the conditions below, and to the best of my knowledge is not subject to any infirmity, physical or mental, to such a degree as to interfere with the efficient discharge of his or her duties arising in relation to the employment covered by this certificate.

EXTENT OF EMPLOYMENT COVERED BY THIS CERTIFICATE

Name of operator …………………………………………..

Address of operator ………………………………………………………………………….

Name of Mine………………………………………………………………………………….

(Extent of employment in the mine, insert either “All kinds” or specify the particular department, processes or kinds of work to which the certificate is confined)

      - ……………………………………..

      - ……………………………………..

      - ……………………………………...

      - ……………………………………..

      - ……………………………………..

CONDITIONS ATTACHED TO THIS CERTIFICATE

- If none, insert “none” ……………..

- If granted subject to re-examination within 12 months insert date; Re-examine before…………………….

- If granted for a limited period, the date on which the certificate will expire; …………….

Name of Doctor …………………………………………..

Address of Doctor ………………………………………………………………………….

Date………………………………………………………………………………….

GIVEN under my hand,

2010

Minister of State at the Department of Enterprise, Trade and Employment.

EXPLANATORY NOTE

(This note is not part of the Instrument and does not purport to be a legal

interpretation)

These Regulations set out requirements with respect to safety, health and welfare in mines, as defined in Regulation 3, and replace a range of provisions formerly applied in the Mines and Quarries Act 1965 and in various Regulations made under that Act.

The Regulations also retranspose, in relation to mines, the relevant provisions of Council Directive 92/104/EEC of 3 December 1992 on the minimum requirements for improving the safety and health protection of workers in surface and underground mineral extracting industries (OJ L404, 31.12.1992, p. 10).

The Regulations come into operation on …… …………. 2010.

The Regulations apply to all mines where persons work and set out duties on the operator, mine manager, deputies (shiftbosses) and employees at a mine with respect to persons at or in the area immediately surrounding a mine.

The Regulations—

(a) in Part 1, which relates to preliminary and general provisions, provide for the commencement of the Regulations, set out various definitions, provide for the application of the Regulations and provide that the Safety, Health and Welfare at Work (Extractive Industries) Regulations 1997 (S.I. No. 467 of 1997) do not apply to a mine as defined in Regulation 3 of these Regulations (Regulations 1 to 5),

(b) in Part 2, which relates to safety and health management—

(i) set out requirements relating to the appointment of mine operators, notifications to the Health and Safety Authority and set out general duties on the operator to take the measures necessary to ensure, so far as is reasonably practicable, that the mine can be worked without risks to safety, health and welfare (Regulations 6 to 9 and Schedule 1),

(ii) apply duties on the operator with respect to establishing a management structure and preparing a safety statement and set out the qualifications for and duties of a mine manager (Regulations 10 to 13),

(iii) set out the co-ordination role of an operator appointed under Regulation 6, require the operator to ensure that workers are competent (including mines skills training and certification), set out the qualifications for and duties of deputies (shiftbosses) (Regulations 14 to 18 and Schedules 2 and 3),

(iv) require that instructions, rules and operating procedures designed to secure safety, health and welfare are in place, set out requirements regarding permits to work, duties of persons at work, consultation with mines safety representatives and employees and record keeping (Regulations 19 to 24 and Schedule 4),

(c) in Part 3, which relates to inspection and supervision, set out requirements relating to inspection, maintenance and testing schemes, supervision of work, pre-shift inspections and inspections during shifts (Regulations 25 to 28),

(d) in Part 4, which relates to roads and vehicles, set out requirements relating to construction and equipment of vehicles, inspection and maintenance of vehicles appointment of drivers, carrying of passengers, road surfaces, roadway clearances, gradients, safety of pedestrians in roadways, vehicle and traffic rules, safeguarding edges of excavations and lagoons, danger areas, traffic routes, outdoor workstations, protection from falling objects and provision of safety helmets and prevention of drowning (Regulations 29 to 43 and Schedule 5),

(e) in Part 5, which relates to ventilation, set out requirements relating to duty to provide adequate ventilation, main ventilation fan,  additional underground, fans, auxiliary ventilation, prevention of leakage and ventilation rules (Regulations 44 to 49),

(f) in Part 6, which relates to stability and ground support, set out requirements relating to general duty to ensure safety of excavations, tips, and lagoons, operating procedures for excavations, tips and lagoons, stability of roads and working places, duty of persons at work in a mine, scaling of roof and sides, working at or near unsupported stopes, the use of backfill material as a means of support, ground support rules, appraisal and site investigation of excavations, tips and lagoons, and geotechnical assessments (Regulations 50 to 59 and Schedule 6),

(g) in Part 7 which relates to explosives, set out requirements relating to application of part 7, appointment of explosives supervisors, shotfirers and storekeepers, scheme of transit for explosives, storage, transport, use and disposal of explosives or ANBI, shotfiring rules, blast specification, shotfiring operations, duties of explosives supervisor and shotfirer, misfires, prohibited activities, and records of explosives (Regulations 60 to 70),

(h) in Part 8, which relates to electricity, set out requirements relating to general, protection of cables, introduction of electrical equipment, restriction of certain categories of electrical equipment in certain zones below ground, cutting off electricity or making safe where flammable gases are found, means of cutting off electricity to circuits below ground, schematic diagrams, electric shock notices, storage, charging and transfer of electrical storage batteries, leakage protection, reportable incidents, and new installations and major alterations (Regulations 71 to 82),

(i) in Part 9, which relates to access, egress and emergency planning, set out requirements relating to outlets and workings, ladderways between working levels, entrances to shafts, staple pits, ore passes and stopes, pedestrian and vehicle traffic routes, escape and rescue facilities, safety drills, fire and explosion hazards, explosive or harmful atmospheres, lighting, prevention of unauthorised entry, means of evacuation, underground workforce accounting, precautions for withdrawal of employees, precautions against external dangers to workings, precautions in case of outbreak of fire, inspection of fire-fighting equipment, warning of emergencies, refuge stations, rescue teams, composition of rescue teams, training of rescue workers, equipment to be provided for rescue work fresh air base, rescue plans, incident controller, and emergency procedures (Regulations 83 to 108 and Schedule 9),

(j) in Part 10, which relates to preparation of mine plans, set out requirements relating to appointment and qualifications of mine surveyor, duties of mine surveyor, scale, datum and other details required on plans, additional plans, keeping of plans, and faulty plans (Regulations 109 to 114),

(k) in Part 11, which relates to provisions relating to hoisting systems (including shafts), set out requirements relating to appointment and hours of work of hoistman, hoisting rules, hoist controls, instrumentation and position indicators, and breaking systems (Regulations 115 to 118 and Schedule 7),

(l) in Part 12, which relates to special provisions relating to gaseous mines, set out requirements relating to protection from explosion risks, gassy mines, mines containing flammable dusts, electrical equipment at gassy mines or mines containing flammable dusts, fires, spontaneous combustion and heatings, gas outbursts, rock bursts and water inrushes, protection from harmful atmospheres, and safety equipment (Regulations 119 to 126),

(m) in Part 13, which relates to air receivers, set out requirements relating to definition of “air receiver”, safety precautions, and maintenance and examination (Regulations 127 to 129 and Schedule 8),

(n) in Part 14, which relates to safety provisions for ancillary activities and installations, set out requirements relating to definition of “place of work” (Part 14), stability and solidity, floors, walls and ceilings of rooms, room dimensions, air space in rooms and freedom of movement at workstations, windows and skylights, doors and gates, ventilation in rooms, and temperature in rooms (Regulations 130 to 137),

(o) in Part 15, which relates to health, set out requirements relating to health surveillance, medical examinations, health hazards, atmospheric influences, disposal of waste, and stationary internal combustion engines and exhaust gases (Regulations 138 to 143 and Schedule 9), and

(p) in Part 16, which relates to welfare, set out requirements relating to shelters and accommodation for clothing and taking meals, changing rooms and lockers, washing facilities, sanitary conveniences, safe access to places where facilities are provided, pregnant women and nursing mothers, persons with disabilities, and rest rooms (Regulations 144 to 151).

A separate Order, the Safety, Health and Welfare at Work Act 2005 (Mines) (Repeals and Revocations) (Commencement) Order 2010, activates the repeal of the Mines and Quarries Act 1965 (No. 7 of 1965) in so far as that Act relates to mines and revokes all Regulations, Orders and Rules made under that Act, as they relate to mines, from …… …………. 2010.

The Safety, Health and Welfare at Work Act 2005 (Quarries) (Repeals and Revocations) (Commencement) Order 2008 (S.I. No.29 of 2008) already activated the repeal of the Mines and Quarries Act 1965, in so far as that Act related to quarries, and revoked all Regulations, Orders and Rules made under that Act, as they related to quarries, from the coming into operation of the Safety, Health and Welfare at Work (Quarries) Regulations 2008 (S.I. No.28 of 2008) on 1 May 2008.

11 January 2010

# Footnotes

OJ No. L404, 31.12.1992, p.10